302 - Flight - Radios, Navigation, Flight Director, Jettison

Radios
COM1	AN/ARC-164(V)	UHF	225.000 to 399.975 MHz	AM	Instrument panel
COM2	AN/ARC-134	VHF	116.000 to 151.975 MHz	AM	Right console

Change active radio with large black knob on AUDIO panel (right console).
ARC-164(V) UHF radio
- UHF radio controls are on left side of front instrument panel.
- Power on by setting Function Dial to MAIN or BOTH.
- Using presets:
  1. Frequency Mode Dial ... PRESET
  2. Change channel with Preset Channel Selector knob. Channel is shown in small window to left of knob, 20 channels available.
  3. Main frequency/channel readout above control panel can show either channel or frequency, use switch to left to toggle.
Changing preset channel frequencies:
1. Select preset channel you want to change.
2. Select frequency you want to set the preset to by tuning it on the frequency knobs.
3. Open the UHF Cover (white panel above frequency knobs) (scroll up) and press the PRESET button to set selected frequency to selected channel.
Manual frequency tuning:
1. Frequency Mode Dial ... MANUAL
2. Set frequency with knobs.
ARC-134 VHF radio
- VHF radio controls are on right console rear.
- Power on by setting Power switch to ON (forward).
- Manual frequency tuning (no presets available):
Set frequency with knobs.

Navigation
     VOR TACAN VORTAC VOR-DME NDB NDB-DME
NDB with ADF receiver
No ADF receiver on the C-101EB. (UHF radio has an ADF mode, but manual says it's inoperative.)
VOR with VOR-ILS-MB receiver
1. On VOR-ILS-MB panel (right console):
  1. NAV/VOL knob ... Turn on and adjust volume as desired
  2. Tune VOR frequency with tuning knobs.
2. Verify NAV button is lit (button to left of HSI), which means it's using the receivers in your cockpit and not the other one.
3. Set HSI to VOR (button to left of HSI, toggles VOR/TAC). (Sets source for CDI needle.)
4. Set desired course to VOR using Course Select Remote Control knob (course knob on HSI panel on right console rear, or Middle Finger Hat up/down).
5. Thin white needle in RMI compass points to VOR beacon. HSI also shows course deviation with displaced yellow line in the middle.
TACAN
1. On TACAN panel (right console):
  1. Mode knob ... REC, T/R, A/A REC, or A/A T/R as needed
  2. Tune TACAN channel with tuning knobs.
2. Verify NAV button is lit (button to left of HSI), which means it's using the receivers in your cockpit and not the other one.
3. Set HSI to TAC (button to left of HSI, toggles VOR/TAC). (Sets source for CDI needle.)
4. HSI will now show distance to TACAN station in top right readout.
5. Set desired course to TACAN using Course Select Remote Control knob (course knob on HSI panel on right console rear, or Middle Finger Hat up/down).
6. Double-line yellow needle in RMI compass points to TACAN beacon. HSI also shows course deviation with displaced yellow line in the middle.

Flight Director -- TODO
NOTE: Flight Director is not an autopilot, it just provides steering indicators.

Jettison
Nothing to jettison on the C-101EB.