201 - Ground - Cold Start - Pilot

Cold Start Checklist for Pilot -- (Auto Start is as fast or faster)
1. OXYGEN switch ... ON (forward) (left elbow console extreme rear)
2. Ground Crew, Ground Electric Power ... On
3. Ground Crew, Ground Air Supply ... On
4. Jester menu ... Startup
5. When Jester calls "ICS comm check": Jester menu ... Loud and Clear
6. Ejection Seat ... Arm (switch at top center of headrest)
7. Jester closes canopy.
8. Jester calls "Ready to start" or similar.
9. Start right engine:
  1. Engine Crank switch ... Right (right click) (left console forward, outboard of throttle)
  2. When RPM is 30%: Right throttle ... Idle (Bottom Thumb Button)
  3. Engine should stabilize at 70% RPM.
10. Start left engine:
  1. Engine Crank switch ... Left (left click) (left console forward, outboard of throttle)
  2. When RPM is 30%: Left throttle ... Idle (shift-Bottom Thumb Button)
  3. Engine should stabilize at 70% RPM.
11. Ground Crew, Ground Electric Power ... Off
12. Ground Crew, Ground Air Supply ... Off
13. VDI, HUD, and HSD power switches... ON (switches on forward right panel, bottom)
14. All SAS switches ... ON (left console outboard) (shift-Pinky Switch up/down/press)
15. Set HSD to TID display (T4 down) to monitor INS alignment (forward right panel, middle column):
  - Jester enters coordinates if on ground, or starts carrier alignment.
  - Caret on top moves from left to right as INS aligns, takes about 7 minutes on ground, 9 minutes on carrier, 2 minutes if using stored alignment. ASH (Automatic Stored Heading) on VDI indicates using stored alignment.
  - Number on left is tenths of minutes that the alignment has been running (e.g. 5 minutes = 50)
  - First tick mark is Coarse Alignment Complete, and aircraft can be flown, but Sparrow and Phoenix will only work in boresight modes.
  - Second tick mark is Alert Launch Criteria, and allows Sparrow and Phoenix non-boresight modes. Caret becomes a diamond at this tick.
  - Third tick mark is Fine Alignment Complete, and indicates full-accuracy alignment. Caret becomes a dotted diamond at this tick.
1. Backup ADI ... Uncage (left click knob) (right side of instrument panel)
2. Radar Altimeter ... On and set altitude bug (scroll wheel on adjustment knob) (left side of instrument panel)
  - Takes a bit to warm up.
1. If on shore, unsweep wings (if on carrier, wait until directed or on catapult):
  1. Emergency Wing Sweep Lever ... Move to 68 deg position, wait 10 seconds, then move all the way forward and push down (left console inboard from throttle)
  2. Emergency Wing Sweep cover ... Close (left console inboard from throttle)
  3. MASTER RESET button ... Press (forward left panel, bottom, just in front of Emergency Sweep lever)
  4. Wing Sweep ... Auto (Top Hat up)
2. Radio ... BOTH (left console behind throttle)
3. TACAN ... T/R (left console behind throttle)
4. When INS is aligned: Jester calls "Ready to taxi" or similar.
5. Parking brake ... Disengage (push in) (black and yellow striped handle on left front panel outboard)

Proceed with rest of preflight checklist on next page.