501 - A/G - Pilot - Unguided Bombs, Rockets

Master Arm ... ON
Display Mode button ... A/G (Mode dial 4), may take 30 seconds to display symbology

All
In A/G mode, the TV camera is slaved to the CCIP pipper or the CCRP target designator diamond. Set the VDI MODE switch to TV to see the camera view of the target area.

Gun strafing
1. Weapon Selector switch ... GUN (Dish Hat up/down)
2. GUN RATE button ... As desired (UFC)
3. CCIP pipper should appear when pointing at the ground. Press Trigger to fire.

CCIP bombing
Jester: Air To Ground/Weapons, then go through the settings to select and configure bombs as needed. Current configuration is shown in the center of the Jester menu wheel.
  - You need to be in CMP/PLT mode for CCIP, use Set Computer Target/Set Computer Pilot to toggle.
  - Note that "Set Ripple Distance" is actually a timing calculated by Jester based on current speed; there is no true ripple distance setting in the F-14.
1. Weapon Selector switch ... OFF (Dish Hat down)
2. Selected stations should show checkerboards in indicators above VDI.
3. Wing Sweep ... Bomb (55 deg) (shift-Top Hat down)
4. Dive on bomb fall line, put pipper on target.
5. Press Red Button to drop.

CCRP bombing with visual designation
Jester: Air To Ground/Weapons, then go through the settings to select and configure bombs as needed. Current configuration is shown in the center of the Jester menu wheel.
  - You need to be in CMP/TGT mode for CCRP, use Set Computer Target/Set Computer Pilot to toggle.
  - Note that "Set Ripple Distance" is actually a timing calculated by Jester based on current speed; there is no true ripple distance setting in the F-14.
1. Weapon Selector switch ... OFF (Dish Hat down)
2. Selected stations should show checkerboards in indicators above VDI.
3. Wing Sweep ... Bomb (55 deg) (shift-Top Hat down)
4. Press Middle Finger Hat up/down to move target diamond along bomb fall line over the target.
5. Press Middle Finger Hat right to lock the target. Once locked, it cannot be adjusted, only unlocked.
Press Middle Finger Hat right again to unlock and slave target designator to velocity vector.
1. Fly to get velocity vector lined up on the bomb fall line.
2. Lower Solution Cue (short horizontal line) will start dropping down the bomb fall line.
3. Hold Red Button.
4. Then Upper Solution Cue (slightly longer horizontal line) will start dropping down the bomb fall line. Bomb drops when Upper Solution Cue meets velocity vector.

CCRP toss bombing
1. Follow steps above to set up weapons and designate target visually.
2. When Lower Solution Cue starts falling down the bomb fall line, pull up to about 30 degrees, stabilize, and hold Red Button until the Upper Solution Cue drops down to meet the velocity vector and bombs away.

Rockets
Jester: Air To Ground/Weapons, then go through the settings to select and configure rockets as needed. Current configuration is shown in the center of the Jester menu wheel.
  - You need to be in CMP/PLT mode for CCIP, use Set Computer Target/Set Computer Pilot to toggle.
  - Note that "Set Ripple Distance" is actually a timing calculated by Jester based on current speed; there is no true ripple distance setting in the F-14.
1. Weapon Selector switch ... OFF (Dish Hat down)
2. Selected stations should show checkerboards in indicators above VDI.
3. Wing Sweep ... Bomb (55 deg) (shift-Top Hat down)
4. CCIP pipper should appear when pointing at the ground. A diamond appears inside the pipper when you're out of range. When the diamond disappears, press Trigger to fire.