501a - A/G - RIO - Unguided Bombs, Rockets

Stations
- 1A -- left wing glove upper rail (AIM-9 only)
- 1B -- left wing glove lower rail
- 2 -- under left engine nacelle (fuel tank only)
- 3 -- left front tunnel
- 4 -- left rear tunnel, or center rear tunnel (Sparrow)
- 5 -- right rear tunnel, or center middle tunnel (Sparrow)
- 6 -- right front tunnel
- 7 -- under right engine nacelle (fuel tank only)
- 8B -- right wing glove lower rail (LANTIRN pod goes here if fitted)
- 8A -- right wing glove upper rail (AIM-9 only)

Bombing -- All modes, weapon setup
1. WPN TYPE selector ... As needed (front right console, top)
2. ATTK MODE dial ... As needed (see different bombing modes below)
3. DLVY MODE switch ... As desired (STP for one pulse per pickle, RPL for more than one pulse while pickle is held, SGL for single bombs, PRS for pairs)
4. MECH FUZE switch ... NOSE or NOSE/TAIL
5. ELEC FUZE knob ... As desired (usually INST)
6. DLVY OPTNS ... As desired: INTERVAL in msec x 10 (implied trailing zero shown after the dial), and QTY
7. STA SEL switches ... As needed

CCIP bombing
ATTK MODE dial ... CMPTR / PLT

CCRP bombing with visual designation by pilot
ATTK MODE dial ... CMPTR / TGT

CCRP bombing with pre-planned waypoint designation -- WIP
1. ATTK MODE dial ... CMPTR / IP
2. Set up attack waypoint and offset:
  1. CAP selector ... TAC DATA
  2. CAP OSB ... IP

Rockets -- WIP
1. WPN TYPE selector ... As needed (front right console, top)
2. ATTK MODE dial ... CMPTR / PLT for CCIP mode
3. DLVY MODE switch ... As desired (STP for one pulse per pickle, RPL for more than one pulse while pickle is held, SGL for single bombs, PRS for pairs)
4. MECH FUZE switch ... NOSE or NOSE/TAIL
5. ELEC FUZE knob ... As desired (usually INST)
6. DLVY OPTNS ... As desired: INTERVAL in msec, and QTY
7. STA SEL switches ... As needed