031 - Flight - Preflight, Takeoff, Landing, Performance Limits

To Rearm and Refuel, you must have engines off and canopy open
1. Shift-Bottom Thumb Button press to turn off engines.
2. T7 up to toggle canopy.
3. When done, Bottom Thumb Button press to start engines. Make sure electrical power is on (T1 switch) and throttle is at idle.

Before takeoff
1. Canopy ... Closed
2. Air brakes ... Closed
3. RWR settings and volume ... As needed

Takeoff
1. Flaps ... Down.
2. Brakes will hold about 80% RPM.
3. Begin takeoff run.
4. Gently rotate at 160 kts to 10-12 degrees, no more than 14 degrees or risk tail strike.
5. Takeoff will be around 180 kts with full load (missiles and 3 tanks).

Climb
- Mil power: 350 kts to 0.9 Mach, then maintain 0.9 Mach.
- Max power (AB): 350 kts to 0.95 Mach, then 40 degrees maximum pitch.

Landing
1. Under 250 kts, put down gear and flaps.
2. Landing speed: ??

RWR
- Diamond is most important threat.
- Flashing Circle is locked on to you.
- Flashing Circle around Diamond with M is incoming ARH missile.
- Pointy Hat is airborne target.
- Semicircle Over Top is SAM or ground threat.
- + in the middle is ECM off, * in the middle is ECM on.
Press Shift-E1 press to toggle RWR on/off, Shift-E1 rotate to adjust volume.

Performance limits
- Fuel: 13455 lbs internal
  - with 3x drop tanks (4114 lbs ea.) = 25795 lbs
- Landing gear and flaps: 250 kts??