1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

201 - Ground - Manual Cold Start

Manual Cold Start and Preflight Checklist -- WIP, needs verification and optimization
1. L and R GEN switches ... ON (right console forward inboard)
2. L and R ENG CONTR switches ... ON (right console forward middle)
3. L and R ENG MASTER switches ... ON (right console forward, black guarded switches)
4. STARTER switch ... ON (right console forward)
5. AIR COND switch ... AUTO (right console forward outboard)
6. L and R INLET switches ... AUTO (left console forward outboard)
7. JET FUEL STARTER handle ... Pull (left click) (right lower instrument panel)
8. When READY light by STARTER switch turns on (green) (about 5 seconds), proceed.
9. Start right engine:
  1. On right engine throttle, raise fingerlift to begin spooling.
  2. Watch engine monitor. When RPM reaches 26%, move right engine throttle to IDLE.
  3. Wait for engine to spool up to 72%.
10. UFC brightness ... As desired (knob on UFC)
11. Radios ... ON (press and release volume knobs) (UFC)
12. Start left engine:
  1. On left engine throttle, raise fingerlift to begin spooling.
  2. Watch engine monitor. When RPM reaches 26%, move left engine throttle to IDLE.
  3. Wait for engine to spool up to 72%.
13. Canopy ... Close and seal (lever on right canopy rail)
14. BRAKEHOLD switch ... ON (right lower instrument panel)
  - BRAKEHOLD must be on for INS alignment.
INS knob ... STORE for stored heading (1 min), or GC ALIGN for full alignment (4 mins)
  - Alignment progress is shown on bottom right of HUD.
  - For stored heading, will show SH NO TAXI, then SH OK.
  - For full alignment, will show GC NO TAXI, then GC nn.n, where nn.n is the current accuracy. As accuracy improves (number gets smaller), will eventually go to GC OK.
  - IMPORTANT: Do not rearm or move the controls (especially rudder/NWS) while aligning.
  - Once its says SH OK or GC OK, set INS knob to NAV.
1. On PP-EGI page on UFC (showing by default), check lat/long against the initial position shown in kneeboard.
2. BINGO fuel ... As desired (4000 lbs is a good default) (right lower instrument panel, knob on fuel gauge)
3. OXYGEN supply switch ... ON (right console forward)
4. MFDs ... ON (click the rocker switch on each MFD)
5. HUD ... ON and brightness as desired (knob on UFC)
6. TF RDR switch ... STBY (left console middle, behind throttle)
7. RDR ALT switch ... ON (left console middle, behind throttle)
8. RADAR switch ... ON (radar will stay off while weight-on-wheels) (left console middle, behind throttle)
9. NAV FLIR switch ... ON (turns on NAV FLIR for use in both MFD and HUD) (left console middle, behind throttle)
10. NAV FLIR GAIN/BRIGHTNESS knob ... As desired (left console middle) (only affects HUD repeater)
11. JTIDS knob ... NORM (left console middle, behind throttle)
12. CAS YAW, ROLL, and PITCH switches ... ON (left console forward inboard)
13. SAI (Standby Attitude Indicator) ... Uncage and center (left lower instrument panel)
14. Backup altimeter ... Set to match QNH (current altitude above sea level)
15. Ejection seat ... ARM (lever on left forward base of seat)
16. Set up back seat:
MFDs and backup instruments:
  1. All MFDs ... ON
  2. SAI (Standby Attitude Indicator) ... Uncage and center (left lower instrument panel)
  3. Backup altimeter ... Set to match QNH (current altitude above sea level)
Left console:
  1. TGT FLIR switch ... STBY (left console middle)
  2. LASER switch ... ARM (left console middle)
  3. RWR/ICS switch ... COMBAT (left console)
  4. ICS switch ... AUTO or MAN (both do the same thing??) (left console)
Right console:
  1. OXYGEN supply switch ... ON (right console forward, in front of right hand controller)
  2. ICS switch ... ON (right console middle)
  3. RWR switch ... ON (right console middle)
  4. EWWS switch ... ON (right console middle)
  5. CMD MODE knob ... MAN ONLY?? (right console middle)
  6. Ejection seat ... ARM (lever on left forward base of seat)
2. When HUD says SH OK or GC OK in lower right, INS is aligned: INS knob ... NAV
3. BRAKEHOLD switch ... OFF (right lower instrument panel)
Proceed with General Preflight checklist on other page...