1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

202 - Ground - Auto Cold Start

Run Auto Cold Start with LWin+Home, takes 3m20s.

After Auto Cold Start, Preflight checklist
BRAKEHOLD switch ... ON (right lower instrument panel)
  - BRAKEHOLD should be on during INS alignment.
INS knob ... STORE for stored heading (1 min), or GC ALIGN (gyrocompass) for full alignment (4 mins)
  - Alignment progress is shown on bottom right of HUD.
  - For stored heading, will show SH NO TAXI, then SH OK.
  - For full alignment, will show GC NO TAXI, then GC nn.n, where nn.n is the current accuracy. As accuracy improves (number gets smaller), will eventually go to GC OK.
1. MIC switch ... ON (left console outboard)
2. JTIDS knob ... ON (left console)
3. Radar mode selector knob ... ON (left console)
4. NAV FLIR switch ... ON (left console)
  - Should be on even during daytime so WSO can use it on HUD repeater page.
1. AUTO NCTR switch ... ON?? (left console extreme outboard)
2. Lights ... As desired:
  1. HUD brightness knob on bottom left of UFC
  2. External light panel on left console just aft of throttle
  3. Internal light panel on right console outboard
3. Rear cockpit switches:
  1. TGP power switch ... ON (left console)
  2. LASER power switch ... ON (left console)
  3. RWR/ICS switch ... COMBAT (left console)
  4. MIC switch ... ON (left console)
  5. ICS operational mode switch ... AUTO or MAN (both are actually automatic??) (left console)
  6. ICS on/off switch ... ON (right console)
4. Hold down T/O TRIM button (Trim Hat press, or left console forward) until TRIM light turns green and voice warning "YAW RATE" (about 3-4 seconds)
5. BRAKEHOLD switch ... OFF (right lower instrument panel)

Proceed with General Preflight checklist on other page...