1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

300 - Flight - Aircraft Info, Performance Limits

Aircraft Info
- Fuel:
  - Internal only: ~13,100 (58%)
  - CFTs: ~4,750 each, ~9,500 lbs total
  - Internal with CFTs: 22,588 lbs
  - Droptanks (each): 3,965 lbs
  - Internal with CFTs and 1 droptank: 26,553 lbs
  - Internal with CFTs and 2 droptanks: 30,518 lbs
  - Internal with CFTs and 3 droptanks: 34,483 lbs
- If AOA is above 25 units, speedbrake will not extend.
- Tested max speeds and fuel flows (all testing done with ISA conditions, max fuel, unlimited fuel)
Alt	Mil power					Max power
	KCAS	KTAS	Mach	fuel/eng	fuel tot	KCAS	KTAS	Mach	fuel/eng	fuel tot
Clean, all pylons on, no pods
SL	627	--	0.949	13.4	26.8	732	--	1.107	85.1	170.2
Both pods, 4x Mk 84, 2x gas, 2x AMRAAM, 2x Sidewinder, no center pylon
SL	579	--	0.876	11.8	23.6	683	--	1.034	78.4	156.8
25k	402	563	0.936	7.4	14.8	488	682	1.134	36.4	72.8
30k	352	538	0.912	5.5	11.0	452	669	1.135	29.9	59.8
36k	Can't sustain level flight					401	652	1.133	24.0	48.0

Performance limits
- Landing gear: 250 KCAS (any configuration), 300 KCAS (A/A config without LANTIRN pods)
- Flaps: 250 KCAS
  - Flaps will automatically retract at 250 kts, and re-extend at 230 kts if the flaps switch is down; they will not be damaged by overspeed.
- Tires:
  - Main: 227 kts
  - Nose: 210 kts
- Negative G: 7 sec max
- TFR speed: 370 KCAS/400 kts GS to 0.9 Mach (590 KCAS) to avoid TF algorithm inaccuracies
- Airspeed limits (all with CFTs installed):
  - No LANTIRN pods: 0-36,000 ft: 700 KCAS; 36,000+ ft: Mach 2.0
  - One LANTIRN pod: 0-5,000 ft: Mach 1.0; 5,000-20,000 ft: 625 KCAS; 20,000+ ft: Mach 1.3
  - Two LANTIRN pods: 0-32,000 ft: 700 KCAS; 32,000-48,000 ft: Mach 1.8; 48,000+ ft: decreases with alt up to Mach 1.0 at 70,000 ft