1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

301 - Flight - Takeoff, Climb, Landing, ILS, Engine restart

Takeoff
Hold down T/O TRIM button (Trim Hat press, or left console forward) until TRIM light turns green and voice warning "YAW RATE" (about 3-4 seconds)
1. Flaps down.
2. Use full AB for takeoff.
3. Stick 1/2 back to rotate, 12 deg pitch, see speeds below. WARNING: Easy to over-rotate, be gentle.
  - For smooth rotation and takeoff, as soon as the nose starts coming up, quickly but smoothly relax stick to neutral.
1. Gear and flaps up before 250 kts.
2. Trim nose down or as needed.
Rotation and takeoff speeds for full AB (speed variation due to CG position):
Weight (lbs)	Rotation (KIAS)	Takeoff (KIAS)
40,000	110	149-154
45,000	115-118	154-159
50,000	120-125	158-163
55,000	125	161-163
60,000	130-133	165-169
65,000	140-145	171-177
70,000	155-160	183-190
75,000	160-165	178-194
81,000	167-172	192-199

Climb
- Mil power: Maintain 350 kts (or 300 kts if very heavy/draggy) to 0.90 Mach. Then maintain 0.90 Mach to cruise altitude.
- Max power (AB): Maintain 350 kts to 0.95 Mach (or 0.90 Mach if very heavy/draggy). Then maintain Mach until cruse altitude

Landing
1. Under 250 kts, gear and flaps down.
2. Airbrake optional.
3. On-speed AOA is 20-22 units, 23 units maximum.
4. Over end of runway, cut throttle and flare, touchdown with minimum vertical velocity.
5. Keep 12 deg pitch after touchdown for aerobraking.
6. Keep flaps down and full aft stick for additional drag while braking (from the Dash 1 manual).
7. Apply full brakes for best braking performance.
8. After stopping: retract airbrake and reset takeoff trim (Trim Hat press until "YAW RATE")

ILS landing -- WIP, haven't tested yet
ILS has two modes: ILST and ILSN. ILST uses TACAN station for distance, ILSN uses Sequence Point.
1. For ILST, enable TACAN following steps in other section. For ILSN, select a Sequence Point that is at the desired airfield (or point "B" for the home airfield).
2. On UFC DATA 2 menu, enter ILS frequency on scratchpad (decimal point and trailing zeros optional), then press L3 OSB to enter.
3. On HSI, set nav mode to ILST or ILSN.
4. Set CRS to runway heading.
5. ILS needles are shown in HUD and ADI page.
6. Fly the needles to touchdown.

Engine restart
1. As soon as engine flames out and begins spooling down:
  1. Ideally, maintain 350 KCAS. At least 250 kts below 25,000 ft, or 275 kts above 25,000 ft.
    - If RPMs drop below 12%, maintain 450 KCAS.
  1. Throttle ... MIDRANGE
  2. Wait for automatic relight.
2. If FTIT exceeds 870 deg C, or no FTIT rise within 20 seconds:
  1. Throttle ... OFF
  2. Increase airspeed to 400 KCAS / 0.9 Mach.
  3. When FTIT decreases below 870 dec C: Throttle ... MIDRANGE