1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

302 - Flight - Autopilot, AOA, Air Refueling

AOA rules of thumb
- 8-10 units for best acceleration
- 14/14.5 units for max range cruise (up to/above 25,000 ft)
- 18/17 units for max endurance (up to/above 25,000 ft)
- 16-22 units for optimum, energy-sustaining turns
- 20-22 units for landing on-speed
- 28-30 units for best turn rate (full aft stick to either G limit or 30 units AOA)
- 30 units max AOA

Autopilot
- Press A/P button on UFC to turn autopilot on and show the Autopilot menu.
  - Press A/P button again or press Paddle Switch (Brake Lever) to turn the autopilot off.
  - Initial A/P mode (ATT or HDG) depends on current pitch and roll.
- First line of the Autopilot menu shows the current mode: OFF, HDG, ATT, ALT; or one of the "blended" modes: HDG, NAV, GT, CRS, TCN.
- Press L2 OSB to toggle Steer Mode coupling (couples with Steering Mode set on HSI page).
  - NOTE Must be in NAV Master Mode to engage steering couplingp
- Press L3 OSB to toggle Altitude coupling.
  - With Altitude coupling on, press L4 OSB to toggle BARO or RAD altitude.
  - Press R3 OSB to select an altitude to hold, 1,000 to 50,000 ft (or "10" to "50"). Plane will climb or dive, trying to hold constant airspeed to constant Mach as shown next to R4 OSB.

Air Refueling
1. Pilot Director Lights on the bottom of the tanker tell your position. The lights within the bars show your position relative to the tanker and the refueling position. Fly opposite the direction of the lights to correct your position.
2. Left light is your vertical position. If light is forward of center, you are too low and you need to go up. If light is aft of center, you are too high and you need to go down.
3. Right light is your horizontal position (forward/aft). If light is forward of center, you are too far forward and need to go back. If light is aft of center, you are too far aft and need to go forward.