1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

304 - Flight - Radios, Countermeasures, Jettison

Radio setup and tuning
COM1	ARC-164	UHF	225.000 to 399.975 MHz	AM
COM2	ARC-210	Multi	30.000 to 87.975 MHz / 108.000 to 115.975 MHz / 118.000 to 173.975 MHz / 225.000 to 399.975 MHz	FM / AM / AM / AM

Preset channels:
Enter channel number on UFC scratchpad, then press the channel select knob for desired radio.
Manual frequencies:
Enter frequency on UFC scratchpad, then press OSB next to desired radio display (L5 or R5 OSB).
Other:
Press GREC button to toggle monitoring Guard frequency (243.000 MHz)

Countermeasures setup
1. Press Countermeasures Hat forward or aft for MAN 1 (fixed program), or up or down for MAN 2 (program determined by TEWS).
2. MAN 1 program is 8x chaff and 8x flares, in 2-4-2 pattern??

Jettison
- Emergency jettison:
  - EMERG JETT button (press and hold for 1 second) jettisons everything that can be jettisoned, including the entire wing pylons and all their stores, and the centerline store and pylon. Will not jettison the LANTIRN pods. Master Arm does not have to be on.
- Selective jettison:
  - Must have Master Arm ON to selective jettison.
  - Selective jettison knob on ARMT panel has two sections: MAN and SEL JETT. When you put the knob on one of the SEL JETT settings, the JETTISON screen comes up on the center MFD (or on the ARMT MFD page if you bring that up on another MFD). A/A allows you to select the wing pylons (will jettison the entire pylon). A/G allows you to select A/G stores, racks, or pylons.
  - COMBAT setting:
    - On any MFD, go to ARMT -> CBT JETT page. You can set up 2 jettison programs. Select program with B1 and B2 OSBs.
    - Select program 1 OSB (selected by default), select stations and type you want to jettison, then press ENTER OSB (B5 OSB) to store.
    - Select program 2 OSB and set that up as above, pressing ENTER OSB to store.
    - When Selective Jettison knob is set to COMBAT, first press of JETT button will execute program 1, second press will execute program 2.
    - Recommended to set program 1 to be fuel tanks, program 2 to be A/G armament.
  - Selective jettison knob settings
    - FF (MAN)
    - RET (MAN)
    - REL (MAN)
    - OFF
    - COMBAT (SEL JETT)
    - A/A (SEL JETT)
    - A/G (SEL JETT)