1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

306 - Flight - Navigation information and displays

Navigation information on HUD
- Small circle is drawn at Sequence Point location (or diamond for Target Point).
- Nav data block in lower right shows steering mode and currently selected Sequence Point, distance in nmi, and ETE or ETA (toggle in UFC DATA 1 menu).

Navigation information on HSI
- Current Sequence Point bearing pointer is small blue triangle on outside of compass ring.
- Current Sequence Point location is shown as a small blue circle (adjust range with RNG OSBs). Only currently selected point is shown, unlike on TSD.
- If AUTO SEQ is boxed, next Sequence Point will be automatically selected when flying past current point.
- Nav data block in lower right shows steering mode and currently selected Sequence Point, bearing and distance in nmi, and ETE or ETA (toggle in UFC DATA 1 menu??).
- Change steering mode (what is used for navigation destination) with OSBs:
  - HDG -- Navigate to commanded heading. Change heading with L1 and L2 OSBs (press to increment, or take value from scratchpad). Not fully functional yet.
  - ALG -- Autonomous Landing Guidance. Not implemented yet.
  - TCN/CRS -- TACAN or Course through selected Sequence Point, press to toggle. See other section for TACAN navigation.
  - ILST -- ILS using TACAN station as distance reference. See other section for ILS landing.
  - GT -- Ground Track. Wind-corrected heading using HDG and CRS. Wind direction comes from data in UFC DATA menu. TODO more details...
  - ILSN -- ILS using distance to airfield Steer Point as distance reference. See other section for ILS landing.
  - NAV -- Navigate to selected Sequence Point. Default mode. NOTE Command heading cannot be changed in NAV mode, it's always fixed to the Sequence Point bearing.

Navigation information on TSD
- TSD shows a moving map and the entire flight plan Route and all points.
- TSD page OSBs:
  - T1 -- no function
  - T2 -- Inverse video, only available on monochrome MFDs. May be better for night.
  - T3 -- Cycles declutter level.
  - T4 -- Increments Sequence Points, or takes Sequence Point from scratchpad.
  - T5 -- Toggles North Up or Track Up.
  - L1 -- Shows rings around selected threat point. Not implemented yet.
  - L2 -- Shows shading overlay showing LOS to selected threat point. Not implemented yet.
  - L3 -- Shows shading overlay showing elevation relative to aircraft. Not implemented yet.
  - L4 -- Shows curved route lines based on bank angle and ground speed. Not implemented yet.
  - L5 -- Selects ground speed to be used with bank angle. Not implemented yet.
  - R1 -- Cycles between 4 zoom levels (1x, 1.25x, 1.5x, 2x) (doesn't affect range selection).
  - R2 and R3 -- Change range scale.
  - R4 -- Record screen. Not implemented.
  - R5 -- MFD menu button.
  - B1 -- Toggles aircraft shown at bottom of display or centered.
  - B2 -- Cycles cueing mode so you can cue a sensor from the TSD. Not implemented yet.
  - B3 -- no function
  - B4 -- Cycles Routes (A, B, or C).
  - B5 -- no function