1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

401 - A2A - Radar display and settings

Radar display and settings
- Upper left text shows BRA (bearing on top, range below) to TDC cursor (aka "ack symbols", "| |")
- Top line of text shows locked target's speed, aspect, and heading.
- Bottom left text shows bullseye bearing/range to cursor
- Bottom line of text shows ownship ground speed on left, airspeed on right.
- May have to change channel letter/number to deconflict radar freqs. (T1 and T2 OSBs) One flight would typically be one one letter, with flight members on different numbers.
- Number on the right of the TDC cursor are top and bottom altitudes of radar scan at the TDC cursor distance.
- Number on left side of TDC cursor when hovering over a target shows target's altitude.
- Move the TDC cursor to top or bottom of scope to change range longer/shorter, 10, 20, 40, 80, 160 nmi.
- Move the TDC cursor to left or right side of scope to cycle azimuth/scan width 60 deg (+/-30) or 120 deg (+/-60).
  - In 60 deg scan, long-press TDC press (> 1 sec) to go to 30 deg (+/-15) scan.
- In TWS mode, az-bump toggles 2-bar 60 deg or 4-bar 30 deg scan. Put TDC over word at bottom left of screen, changes to NARROW, press TDC to go to 6-bar 15 deg scan. To get out of that scan mode, az-bump.
- In TWS mode, press TDC on target to designate it as PDT (Primary Designated Target) with a star. Then put TDC over other targets and press TDC press to set them as SDT (Secondary Designated Targets) with a hollow box. Press Quick Step (Middle Finger Hat/Coolie up) to cycle PDT between the SDTs.
- TWS doesn't track targets through the notch as well as STT does.
- Caret at top of scope indicates targets that are beyond currently shown range.
- Typical config:
  - Long range scan: 4-bar, 120 deg, INLV, FS 1, GMTR CHAF
  - Shorter range scan: 6-bar, 60 deg, INVL, FS 1, GMTR CHAF
- Settings:
Name	OSB	Values	Function
Bars	L2	1, 2, 4, 6, or 8	Total elevation range of radar
PRF	B1	HI, MED, INLV	HI PRF -- long range, large targets, closing targets / MED PRF -- shorter range (80 nmi max), smaller targets, low altitude targets, chasing targets
FS	B3??	0, 1, 2	Frame Store -- Number of full scans after which a contact will be cleared if not detected again.
GMTR	L3	LO, MED, HI, CHAF	Ground Moving Target Rejection / LO - 45 kts, may show false targets or ground targets / MED - 63 kts / HI - 87 kts / CHAF - 95 kts, may eliminate helicopters or slow targets
RGH	B2	on/off	Range Gate High -- Special PRF mode between MED and HI. Rarely used??
VCTR	B3	on/off	Vector search -- Very slow search mode for small RCS targets or very long range.
ENTER	B5	--	Saves current radar settings to MRM or SRM mode (whichever is selected) as its new default.