1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

503 - A2G - TPOD use

LANTIRN TPOD
On TPOD page:
- Set laser code: enter code into scratchpad and press T2 OSB (PB 19) to set.
- Auto/Manual lasing:
  - Press T3 OSB (PB 18) to toggle between ALAS and MLAS.
  - Default ALAS time is CONT (continuous lasing). To change ALAS time, go to ARMT page, A/G, PROG PAGE, ALAS OSB (B3 OSB). With nothing in scratchpad, pressing B3 OSB will toggle ALAS CONT and MLAS. For ALAS time, enter number of seconds before impact to start lasing (1-31) on scratchpad and press B3 OSB, or 0 for CONT.
- Box EXP OSB to allow an extra (digital) zoom level.
- Laser only works below 25,000 ft altitude.
- Max laser range is 13.2 nmi (slant range??).
- Laser status shown in bottom right: L when laser is armed, L flashing when laser is firing, L M when laser is masked (blocked by airplane and can't fire).
- Stabilization modes:
  - SP is Ground Stabilized, STAB is Space (airplane) Stabilized
  - Enter 0 on UFC and press T3 OSB (PB 17) to enter STAB mode
  - Snowplow is a default mode of STAB
- Cursor functions: TGT, MARK, CUE, UPDT; only TGT and MARK are fully implemented
  - TGT makes a designation when TDC is pressed, MARK makes a markpoint.
- R3 OSB toggles T1/T2, which is main screen/setup screen. Setup screen (T2) only has YAW/PITCH/ROLL manual boresighting, manual focus control (up/down arrows), and GRY which shows a gray scale.

TPOD Controls (with TPOD IN CMD)
Front seat:
  - Slew -- TDC ministick
  - Cursor action (Designate/Mark/Cue/Update) -- TDC press
  - Undesignate -- Rear Thumb Button press
  - Zoom cycle -- Gray Reset Hat forward short
  - Laser fire toggle -- Pinky Button press
  - Return to cue point -- Gray Reset Hat back short
  - Snowplow mode -- Gray Reset Hat forward long
  - Toggle tracking (ATRK or PTRK) -- Gray Reset Hat press
  - Toggle space stabilization -- Gray Reset Hat back long
  - Select next Sequence Point (shown under T4 OSB) -- Middle Finger Hat up or T4 OSB
  - Slave to bomb pipper -- (with TPOD IN CMD) Dish Hat press, Dish Hat up, then repeat
- Back seat:
  - TPOD on left MFDs, all controls on Throttle Grip:
    - Take command of Left MPD/MPCD -- Middle Finger Hat left/right
    - Slew -- TDC ministick
    - Set cursor action -- Countermeasures Hat: aft=TGT, up=MARK/CUE, down=UPDT
    - Cursor action (Designate/Mark/Cue/Update) -- Rear Thumb Button ("Trigger full-action")
    - Undesignate -- Bottom Thumb Hat press
    - Zoom cycle -- Bottom Thumb Hat forward short
    - Laser fire toggle -- Pinky Button press
    - Return to cue point -- Bottom Thumb Hat back short
    - Snowplow mode -- Bottom Thumb Hat forward long
    - Toggle tracking (ATRK or PTRK) -- Bottom Thumb Hat press
    - Toggle space stabilization -- Bottom Thumb Hat back long
    - Select next Sequence Point (shown under T4 OSB) -- Countermeasures Hat press or T4 OSB
  - TPOD on right MFDs, all controls on Joystick:
    - Take command of Right MPD/MPCD -- Shift-Dish Hat left/right
    - Slew -- Dish Hat
    - Set cursor action -- Trim Hat: aft=TGT, up=MARK/CUE, down=UPDT
    - Cursor action (Designate/Mark/Cue/Update) -- Trigger Stage 2 ("Trigger full-action")
    - Undesignate -- Gray Reset Hat press
    - Zoom cycle -- Gray Reset Hat forward short
    - Laser fire toggle -- Lower Gray Button press
    - Return to cue point -- Gray Reset Hat back short
    - Snowplow mode -- Gray Reset Hat forward long
    - Toggle tracking (ATRK or PTRK) -- Gray Reset Hat press
    - Toggle space stabilization -- Gray Reset Hat back long
    - Select next Sequence Point (shown under T4 OSB) -- Trim Hat press or T4 OSB