1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

505 - A2G - Unguided Bombs, Gun

Fence in
- A/G Master Mode
- Master Arm ON

Gun strafing
1. Deselect all weapon stations on ARMT page.
2. Take command of the HUD (Dish Hat press, then Dish Hat up, HUD should say IN CMD in lower left)
3. Press Auto Acq Switch aft short (Gray Reset Hat aft short) to get gun pipper.
4. Trigger fires gun.

Bomb setup
- All bombs
  - On ARMT A/G page:
  - CDIP	CCIP mode
  - AUTO	CCRP mode
  - 1/STA	One bomb will be dropped from each selected station with each press of the pickle.
  - STEP	One bomb only will be dropped per pickle, alternating stations if multiple stations are selected.
  - RP SGL	While pickle is held, drops up to QTY bombs, at INTVL, alternating stations if multiple stations are selected
  - RP MULT	While pickle is held, drops bombs from each selected station, up to QTY bombs total, at INTVL ft.
  - FUZING	For Mk 82 Snakeye, Mk 82 AIR, and Mk 84 AIR, TAIL or N/T enables high-drag fins/parachute, NOSE disables the high-drag and drops them as slicks.
  - BOT	Determines which bomb in the string will fall on the target. CTR (default) is center bomb, press to cycle number, or enter on scratchpad.
- CBU-87/-97 special fuzing options
  - On ARMT > A/G LOAD page, when loading CBU-87/-97, press FUZE OSB to burst time, burst height, and spin. Burst time and height are shown on the page, spin numbers are as follows:
SPIN n:	1	2	3	4	5	6
RPM:	0	500	1000	1500	2000	2500

- A/G DLVRY page -- WIP
  - PROG page
    - AT	Along Track bias, positive numbers move impact point long, negative numbers move impact point short (in ft??).
    - CT	Cross Track bias, positive for right, negative for left.
    - TARM	Time to Arm, arm time after dropping, in seconds.
    - ALAS	Auto Lase, time before impact to turn on laser, in seconds (1-31). If scratchpad is blank, pushing OSB toggles ALAS/MLAS

CDIP (CCIP) bombing
1. Set up bombs, see settings above.
2. Put pipper on target, press and hold Red Button to drop.
3. If pipper would be off bottom of HUD, press and hold Red Button to designate target and enter auto CCRP mode until drop.
Mk 82, Mk 84
CCIP is accurate
Mk 20 Rockeye
- Use TIME mode rather than HEIGHT??
- CCIP is accurate in a dive. For low altitude level release (as low as 200 ft), it drops long, recommend dropping short by about 1/2 pipper circle radius.

AUTO (CCRP) bombing
1. Set up bombs, see settings above.
2. Designate target.
3. Fly toward bomb fall line (ASL). HUD shows time to release (TREL).
4. When release cue (short horizontal line) starts coming down the bomb fall line, press and hold Red Button until release cue hits velocity vector and all bombs drop.
Toss bombing
Bombs tend to land long. AT bias of -300 ft seems to be pretty close. Set with ARMT -> A/G -> PROG PAGE, L3 OSB.