1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

301 - Flight - Takeoff, Landing, AAR

Takeoff
1. Turn on NWS to taxi ("AR NWS" light shows in small vertical light stack to right of HUD).
2. On takeoff run, disengage NWS at 70 kts.
3. Takeoff speed is 128 kts to 198 kts depending on weight.
4. Hold 8 to 12° pitch (no more than 13° or risk tailstrike).
5. Gear up before 300 kts.

Landing
1. Don't land like a Hornet, you need to flare!
2. Speedbrake out, and keep it out for landing.
3. Under 300 kts, landing gear down.
4. Establish approach AOA of 11°. Don't use pitch trim to control AOA; adjust throttle instead and FLCS will take care of the trim. VV will usually be in the top half of the "[" AOA bracket (11-13°).
  - Max AOA is 13° (middle of the "[" bracket).
1. Dashed line at -2.5° on HUD is glideslope, place that on the runway overrun area, VV on end of runway.
2. When over the runway overrun, throttle to idle, flare gently (keeping VV just below horizon), touchdown at no more than 13° AOA or risk tail strike.
3. Landing speed is around 155 kts.
4. When main wheels touch, hold pitch up to 13° max for aerobraking.
5. Press and hold speedbrake extend button to command max airbrakes mode.
6. Around 100 kts, allow the nose to fall gently. Apply brakes as needed.
7. After stopping, retract speedbrake.

Air Refueling
1. Pilot Director Lights on the bottom of the tanker tell your position. The lights within the bars show your position relative to the tanker and the refueling position. Fly opposite the direction of the lights to correct your position.
2. Left light is your vertical position. If light is forward of center, you are too low and you need to go up. If light is aft of center, you are too high and you need to go down.
3. Right light is your horizontal position (forward/aft). If light is forward of center, you are too far forward and need to go back. If light is aft of center, you are too far aft and need to go forward.