1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

303 - Flight - Radios

Radio setup and tuning
COM1	ARC-164	UHF	225.000 to 399.975 MHz	AM
COM2	ARC-222	VHF	108.000 to 151.975 MHz	AM

Using preset frequencies:
1. Press COM 1 or COM 2 buttons on UFC. DED will show appropriate radio page.
2. Use Dobber up/down to select the channel/frequency field on the right middle (NOT the bottom field). Enter the preset channel number, then press ENTR.
3. Press RTN to return to main DED page.
Quick change if you're already using a preset channel: On main DED page (press RTN), use Dobber up/down to select the UHF or VHF radio field. Press INCR up/down to flip through the channels. Look at the SRS display to see what frequency you're on.
Changing preset frequencies:
1. Press COM 1 or COM 2 buttons on UFC. DED will show appropriate radio page.
2. Use Dobber up/down to select the channel field on the second to last line. Use INCR up/down to flip through the channels. The current frequency for the selected channel will be shown on the bottom line. Select the channel you want to change.
3. Use Dobber up/down to select the frequency field on the bottom (NOT the field on the middle right). Enter the frequency you want the selected channel to be set to, then press ENTR.
  - This does not change what channel or frequency you're currently tuned to, it only changes the frequency for the channel you have selected on the field above!
Press RTN to return to main DED page.
Using manual frequencies:
1. Press COM 1 or COM 2 buttons on UFC. DED will show appropriate radio page.
2. Use Dobber up/down to select the channel/frequency field on the right middle (NOT the bottom field). Enter the frequency in NNN.NNN format, then press ENTR.
3. Press RTN to return to main DED page.
NOTE: Quick change method mentioned above for channels doesn't work if you're tuned to a frequency manually, it only works if you're tuned to a preset channel.