1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

305 - Flight - Datalink

Primary Datalink Track (PDLT)
It can be useful to set your PDLT to your wingman/lead.
1. Set HSD page as SOI.
2. Move cursor over desired item, then press TMS up.
3. An octagon will appear around the selected item on the HSD page, and an octagon will show the location in your HMD.
4. To undesignate, press TMS down.
5. Press TMS right to cycle PDLT from nearest to farthest.

Send SPI or steerpoint to flight -- WIP
1. With anything but HSD page set as SOI, press Middle Finger Hat right long to send the SPI.
2. With HSD page set as SOI, press Middle Finger Hat right long to send current steerpoint location.
3. What happens when receiving transmission?? Clear with WARN/RESET switch on UFC??