1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

401 - A/A - Radar Modes

Master Arm ... ON
Master Mode ... A/A

Radar Modes
- There are two main radar modes: CRM and ACM. Current mode is shown top row left of radar MFD.
- CRM submodes include all your BVR radar modes like RWS, TWS, SAM (Situational Awareness Mode), as well as A/G modes.
- ACM submodes include all your WVR radar modes with automatic locking like Boresight, Vertical, HUD, and Slew.
- To switch between CRM and ACM either press the CRM/ACM OSB on the MFD and then the OSB for the mode you want, or press the DGFT switch (Pinky Switch up) to enter ACM mode.
- In CRM, switch between RWS and TWS with TMS Right Long.
- To IFF interrogate all targets on the radar screen, press TMS left short (Gray Reset Hat left short); or TMS left long (Gray Reset Hat left long for only the target under the cursor.
- TMS left long also does NCTR. Must be in STT, within 25 nmi, target nose or tail within 30 deg az and el of your nose. NCTR ID appears at top center of radar display.

CRM mode (RWS and TWS)
1. RWS mode:
  1. Set SOI to FCR page (Dish Hat down to toggle SOI between the MFDs).
  2. TMS up on a target will progress in this order:
    1. Search Target (no lock) (small solid box)
    2. SAM (Situational Awareness Mode) with Bugged target (large hollow box with circle around it)
    3. either STT (Single Target Track) if TMS up on the same target again (same as Bugged target)
    4. or DTT (Dual Target Track) if TMS up on a different target (one Bugged target and one without the circle, which is the secondary target); press TMS Right Short to toggle primary/secondary.
  3. TMS down reverses the order, eventually unlocking the target.
  4. Missiles can be launched in SAM, DTT, or STT. They will be launched at the current Bugged target.
  5. STT triggers an RWR warning for the enemy, other modes do not.
2. TWS mode:
  1. Targets progress in this order:
    1. Search Target (small solid box)
    2. Track Target (large solid box)
    3. System Target (large hollow box)
    4. Bugged Target (large hollow box with circle around it, only one of these allowed)
  2. Search Targets become Track Targets automatically after detection on two consecutive radar sweeps.
  3. If there are no System Targets or Bugged Targets, press TMS Right Short to turn all contacts into System Targets. Or press TMS Up to turn only one target into a System Target.
  4. Press TMS Up on a System Target to make it the Bugged Target, or press TMS Right Short to cycle the Bugged Target through all the System Targets in turn.
  5. Press TMS Up on the Bugged Target to transition to STT lock.
  6. Press TMS Down to downgrade targets in turn from Bugged, to System, to Track, to Search Targets.
  7. To fire multiple AMRAAMs: Bug a target, fire, TMS Right Short to cycle Bug to next target, fire, repeat.

ACM mode (auto acquisition):
1. To select ACM mode, press CRM OSB (T1), then ACM OSB (L2) (or enter DGFT Override Mode, see other page).
2. Use TMS hat to change search mode (only when SOI on FCR page):
  - U: Boresight scan (or HMCS), 20 nmi
  - D: If no target locked, Vertical scan; if target locked, Target Reject and radar off (NO RAD)
  - R: HUD scan
  - L: Slew scan 20 high x 60 deg wide, 10 nmi, stabilized to horizon. Slew search area with TDC.
Or FCR page T2 OSB to cycle modes: BORE, 20 (HUD scan), 60 (vertical scan), SLEW

Radar controls and symbology
- Top row of FCR page shows radar mode (e.g. CRM RWS, or CRM TWS, or ACM BORE), NORM/EXP for normal view or expanded (zoomed) view, OVRD for radar silence, CNTL for more radar settings.
- Left side shows selected range, azimuth ("A3" = +/-30 deg off nose, or 60 deg total), and bars ("4B" = 4 bars).
- Bottom left shows ownship location relative to bullseye. Number inside circle is range in nmi to bulls, number below circle is bearing to bulls.
- Datalink contacts can be filtered with Comms Hat inboard/outboard?? Current datalink contacts shows above SWAP in bottom row left (ALL, FTR+, TGTS, NONE).
- Number under radar contacts is contact altitude in thousands of ft.