1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

402 - A/A - Guns, Missiles

Master Arm ... ON
Master Mode ... A/A

Corner speed (best sustained turn rate) ... approx 330 to 440 kts, but fast is better than slow, keep your speed up

Master Modes
- There are 3 main Master Modes: A-A, A-G, and NAV. A-A and A-G are selected with buttons on the UFC; NAV is the mode if neither of those are active.
- There are 2 Override Modes: MSL and DGFT. Those are selected at any time with the Pinky Switch on the throttle up/down (up for DGFT, down for MSL, press to cancel and return to previously selected Master Mode).
  - The Override Modes override whatever Master Mode you currently have selected.
- Each Master and Override Mode saves its own MFD pages, selected weapon, and radar mode/settings. This can be confusing if you change settings without knowing what Mode you're in.
- You can fire A2A missiles in A-A, MSL, or DGFT modes, but different procedures are used for each.
- You can use any of the radar modes in any of the Master or Override Modes, but different Modes have different defaults.

Missiles with A-A Master Mode
1. Select desired missile on SMS page, or press Flip Down Trigger long to toggle missile type.
2. Select desired radar mode on FCR page. Radar will start in CRM RWS mode, or you can select TWS or ACM mode by pressing OSBs.
3. Set SOI to FCR page (Dish Hat down to toggle SOI between the MFDs).
4. Lock (or Bug) the target on radar in RWS, TWS, or ACM mode. For radar use instructions, see other page.
5. Missiles can be launched at the Bugged target in SAM, DTT, or STT, or in TWS mode, or at the locked target (STT) in ACM mode.
  1. STT triggers an RWR warning for the enemy, other modes do not.
  2. AIM-120s can be guided on up to 4 TWS targets simultaneously.
6. Press Red Button to fire.

Guns in A-A Master Mode
In SMS page, press AAM OSB (T1) to change to GUN

Missiles with MSL Override mode
1. Press Pinky Switch down to enter MSL (Missile Override) mode.
2. Only allows shooting missiles, gun cannot be selected.
3. Selects longest-range missiles by default: AIM-120s if loaded, otherwise AIM-9s.
  - Press Flip Down Trigger long to toggle missile type.
1. HUD symbology is generally the same as A-A Master Mode.
2. Press RDR CURSOR/ENABLE (shift TDC press) to toggle SLAVE/BORE?? In SLAVE mode the seekers will be slaved to the radar target. In BORE mode they will not be.
Intended use for MSL mode is to quickly switch (with HOTAS) from A-G mode to A2A missiles and radar for a popup target, and then switch back to A-G mode to continue attack. Aside from being able to be selected from the HOTAS and not allowing gun use, it's the same as A-A Master Mode.

Guns and missiles with DGFT Override mode
1. Press Pinky Switch up to enter DGFT (Dogfight Override) mode.
2. Trigger 2nd stage fires guns, Red Button fires missiles.
3. Selects shortest range missiles by default: AIM-9s if loaded, otherwise AIM-120s.
  - Press Flip Down Trigger long to toggle missile type.
1. Selects ACM radar mode by default and sets SOI to radar.
2. Use TMS hat to change ACM mode (only when SOI on FCR page):
  - U: Boresight scan (or HMCS), 20 nmi
  - D: Unlock target and turn off radar (NO RAD on HUD); if no target locked, Vertical scan.
  - R: HUD scan
  - L: Slew scan 20 high x 60 deg wide, 10 nmi, stabilized to horizon. Slew search area with TDC.
1. HUD symbology is greatly simplified and decluttered for minimal distraction in WVR dogfights.
2. Press RDR CURSOR/ENABLE (shift TDC press) to toggle SLAVE/BORE?? In SLAVE mode the seekers will be slaved to the radar target. In BORE mode they will not be.

Special notes for HMCS (HMD) use
When using AIM-9X, press uncage (Middle Finger Hat press) without locked target to make missile seeker follow your line of sight. You can look at a target, then press uncage (Middle Finger Hat press) again to cage (lock) the missile to that target.