1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

501 - A/G - Radar

Master Arm ... ON
Master Mode ... A/G

Radar Modes
- Radar modes:
  - GM ... Ground Mapping
    - RBM ... Real Beam Mode (faster but lower res)
    - EGM ... Enhanced Ground Map (slower but higher res)
  - EXP ... Expanded
  - DBS1 ... Doppler Beam Sharpening 1
  - DBS2 ... Doppler Beam Sharpening 2
  - GMT ... Ground Moving Target
  - SEA ... Sea/Surface Search
- In GM mode, crosshairs default to your SPI (usually your selected steerpoint). CZ OSB resets to steerpoint.
- SP OSB sets cursor to halfway up the current range of the radar.
- T1 OSB cycles mode
- T2 OSB cycles range setting, AUTO changes range when cursor goes to top or bottom, MAN requires manual range changing with OSBs.
- T3 OSB selects GM sub-modes (NORM, EXP, DBS1, DBS2)
  - NORM ... Default radar view
  - EXP ... 4x zoom on area at crosshairs
  - DBS1 ... 4x zoom on area at crosshairs, with 24:1 sharpening
  - DBS2 ... 64x zoom on area at crosshairs (8 nmi square)
  - Pinky Button on throttle also cycles through these options.
- T4 OSB puts radar in standby and disables emit.
- R2 OSB puts radar in standby and freezes current image on screen
- R3 OSB toggles Snowplow mode
- R4 OSB sets Cursor Zero (moves SPI back to steerpoint)
- R5 OSB cycles SPI-Steerpoint relationship, leave in STP (NAV Master Mode), or TGT or SP (A-G Master Mode). Other settings are for using Offset Aimpoints, Visual Reference Points, or Visual Initial Points.

Ground Mapping EXP/DBS1/DBS2 modes -- WIP
Effective zoom level depends on radar range setting as well as EXP/DBS1/DBS2 mode.

GMT mode -- WIP
Moving targets are overlaid on regular ground map image. Targets are solid white boxes.

Radar controls and symbology
- Top row of FCR page shows radar mode (e.g. CRM RWS, or CRM TWS, or ACM BORE), NORM/EXP for normal view or expanded (zoomed) view, OVRD for radar silence, CNTL for more radar settings.
- Left side shows selected range, azimuth ("A3" = +/-30 deg off nose, or 60 deg total), and bars ("4B" = 4 bars).
- Bottom left shows ownship location relative to bullseye. Number inside circle is range in nmi to bulls, number below circle is bearing to bulls.
- Datalink contacts can be filtered with Comms Hat inboard/outboard?? Current datalink contacts shows above SWAP in bottom row left (ALL, FTR+, TGTS, NONE).
- Number under radar contacts is contact altitude in thousands of ft.