1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

504 - A/G - LGBs, JDAM/JSOW

Master Arm ... ON
Master Mode ... A/G

LGBs with TPOD
1. Select bombs in SMS page.
2. Select CCRP release mode (Flip-down Trigger to cycle, or press OSB at top of SMS page).
3. Use TPOD to designate target. No specific type of track is necessary, laser will fire wherever the crosshairs are.
  - Bomb laser code is set on the ground, engine off, see first kneeboard page for keyboard keys.
  - Default is 1688.
  - Set TPOD to same laser code: On UFC, press LIST button at top, then 0 for MISC, then 5 for LASR, select TGP CODE field, enter the code, press ENTR, then RTN.
1. Follow bomb fall line on HUD as with normal CCRP bombing, and hold Red Button when the release cue line appears, until bomb drops.
2. After bomb is released, HUD will show time until impact at bottom right.
3. Lasing must be done manually with Trigger 1st stage. Start lasing about 10 seconds before impact and continue until bomb hits.

GBU-24 Paveway III with TPOD -- WIP
1. Select bombs in SMS page.
2. Select PRE release mode (T2 OSB).
3. Set up bomb options:
  - R3 OSB -- SGL (Single) or PAIR. If PAIR, use R5 OSB to set spacing in feet??
  - L3 OSB -- Fuzing: NOSE, TAIL, or NSTL
  - L4 OSB -- AD/BA (Arming Delay): Press to cycle arming delay after drop.
  - T5 OSB -- CNTL page:
    - Shows current Time of Flight based on current alt/speed.
    - CUE RNG is the small circle in the DLZ bars. Does not affect actual drop range, only there as a cue or reminder for the pilot for planning purposes.
    - REL ANG is release angle, set to 0 deg for level drop.
  1. Recommended options: SGL (single), NSTL (unless delay is needed), AD/BA = 0s, CUE RNG doesn't matter, REL ANG = 0.
2. Drop whenever you're in the DLZ; short horizontal line will come down the Bomb Fall Line and sit on the velocity vector when you're in range and can drop.
3. Lasing must be done manually with Trigger 1st stage. Lase during the entire fall until it hits.

JDAM/JSOW -- WIP
Select bombs in SMS page, press PWR OFF OSB to change to PWR ON and wait for alignment.
  - Alignment progresses from A10, A09, A08... to RDY when complete.
Select targeting mode: VIS or PRE
  - VIS (Visual) mode uses HUD to designate target visually.
  - PRE (Pre-planned) mode uses Steerpoint or TPOD target.
Press CNTL OSB to set bomb options:
  - PROF n ... Profiles to store sets of options, cycles through 4 profiles.
  - AD ... Arming Delay. Sets the delay between release and weapon arming.
  - AIR/GND/GND DLY ... Sets fuzing for airburst, impact (instant), or delay. If GND DLY is used, additional FD option will appear for Fuzing Delay, the time delay after impact to detonation.
    - IMPORTANT: As of 2023-02-26, only AIR can be selected. This is a bug/WIP.
  - IMP ANG ... Impact Angle, up to 90 deg. High angle may be useful for targets in trees or between buildings.
  - IMP AZ ... Impact Azimuth (heading). Bomb will attempt to be flying this heading on impact. 0 for no specific heading, 360 for due north heading.
  - IMP VEL ... Impact Velocity. Bomb will attempt to be going this speed (ft/s) at impact.
1. Designate a SPI (Sensor Point of Interest aka ground target) either visually through the HUD (VIS mode) or with TPOD, A2G radar, or other means (PRE mode). If using TPOD, no specific type of track (area vs point) is necessary. Any other method of generating a SPI can also be used.
2. Follow bomb fall line on HUD as with normal CCRP bombing. Launch zone symbology is shown on right side of HUD:
  1. Number at top shows range scale in nmi.
  2. Caret is your current range.
  3. Bracket shows min and max range.
3. Press Red Button to drop whenever the current range caret is inside the range bracket.
4. After bomb is released, HUD will show time until impact at bottom right.

CBU-103 (CBU-87 with WCMD) and CBU-108 (CBU-97 with WCMD)
Same as JDAM/JSOW, but shorter range.