1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

505 - A/G - CBU-103/CBU-105 WCMD

Master Arm ... ON
Master Mode ... A/G

CBU-103 (CBU-87 with WCMD) and CBU-105 (CBU-97 with WCMD) -- WIP
Select bombs in SMS page, press PWR OFF OSB to change to PWR ON and wait for alignment.
  - Alignment progresses from A10, A09, A08... to RDY when complete.
Select targeting mode: VIS or PRE
  - VIS (Visual) mode uses HUD to designate target visually.
  - PRE (Pre-planned) mode uses Steerpoint or TPOD target.
Select ripple setting and spacing:
  - Triangles next to each other will release a pair that will dispense beside each other.
  - Triangles fore-and-aft will release a pair that will dispense one behind the other.
  - Distance in feet is how far apart the pair will dispense.
Press CNTL OSB to set bomb options:
  - ATK AZ ... Attack Azimuth (heading). NOT IMPLEMENTED. Bomb will attempt to be flying this heading on impact. 0 for no specific heading, 360 for due north heading.
  - AD ... Arming Delay. NOT IMPLEMENTED. Sets the delay between release and weapon arming.
  - BA ... Burst Altitude. Higher altitude gives greater dispersion.
  - SPIN ... Spin rate before dispensing (CBU-103 only). Higher spin rate gives greater dispersion.
  - TGT WD ... Manual winds aloft entry. NOT IMPLEMENTED.
  - WD SOURCE ... Wind data source. Currently only MP (Mission Planning). Other sources would be PI (pilot entered), SY (avionics system).
1. Designate a SPI (Sensor Point of Interest aka ground target) either visually through the HUD (VIS mode) or with TPOD, A2G radar, or other means (PRE mode). If using TPOD, no specific type of track (area vs point) is necessary. Any other method of generating a SPI can also be used.
2. Follow bomb fall line on HUD as with normal CCRP bombing. Launch zone symbology is shown on right side of HUD:
  1. Number at top shows range scale in nmi.
  2. Caret is your current range.
  3. Bracket shows min and max range.
3. Press Red Button to drop whenever the current range caret is inside the range bracket.
4. After bomb is released, HUD will show time until impact at bottom right.