1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

506 - A/G - AGM-65 Mavericks

Master Arm ... ON
Master Mode ... A/G

Once powered on, missiles have 1 hour in standby mode or 30 minutes showing video, then must be powered off for 2 hours. Use the auto power on feature to turn missiles on automatically after passing a steerpoint.

Mavericks without TPOD
VIS mode - visual targeting f‌irst through the HUD, then f‌inal adjustment in the seeker itself:
1. On right MFD, go to SMS page, select Mavericks, set VIS mode (default), set SOI to HUD.
2. On left MFD, go to WPN page, but don't set it as SOI.
  - Don't set SOI to anything else during this process.
  - Press TMS left to toggle white/black.
  - Press Pinky Button to toggle FOV (only after ground-lock). Uncage button may also toggle FOV??
1. Press TMS down to slave target designator box to VV at any time.
2. Use Ministick to slew square designator box on HUD near target.
3. Press TMS up to ground-lock the designator box and start slewing the Maverick seeker on HUD (circle).
4. Press TMS up again to attempt Maverick lock.
5. If lock fails, center crosshairs on MFD will disappear. Hold TMS up to show crosshairs and slew while holding, missile will attempt to re-lock when you let go of TMS up.
6. When missile is locked (tight crosshairs in the center on the target), fire with Red Button.
BORE mode - similar to VIS mode, but all adjustments are done through the seeker, and the seeker remains f‌ixed relative to the missile, not ground locked (may be useful at night when using missile as a FLIR):
1. On right MFD, go to SMS page, select Mavericks, set BORE mode.
2. Large aiming cross should appear on HUD, showing where seeker is pointing.
3. On left MFD, go to WPN page. (Press TEST OSB twice to bring up pages menu, then WPN to put that page into the slot.)
4. Set SOI to WPN MFD.
5. Use Ministick to slew seeker. It is relative to the airplane, not ground-locked.
6. Press TMS up to attempt Maverick lock.
7. If lock fails, center crosshairs on MFD will disapper. Hold TMS up to show crosshairs and slew while holding, missile will attempt to re-lock when you let go of TMS up.
8. When missile is locked, fire with Red Button.
PRE mode - slaves seeker initially to steerpoint, then you can move it afterwards for the f‌inal lock
TODO

Mavericks with TPOD
Boresighting Mavericks and TPOD (summary: Lock both to same target, press BSGT on Maverick's WPN MFD)
1. Power on Mavericks and TPOD.
2. Set A/G Master Mode, Master Arm to ARM or SIMULATE.
  - If you're on the ground, also set GND JETT switch to ENABLE.
1. On right MFD, go to SMS page, select Mavericks, set PRE mode.
2. On right MFD, go to TGP page and set it to be SOI:
  1. Designate a target with Point track with the TGP (see steps in other checklist for TPOD use).
  2. Target should be in front of the aircraft and at least 1 nmi away to minimize parallax.
3. On left MFD, go to WPN page and set it to be SOI:
  1. Use Ministick to slew Maverick crosshairs to the same target as TGP and press TMS up to lock.
  2. Target must be locked to proceed. If target is locked, BSGT will appear in the MFD.
    - If you can't lock what the TPOD is pointed at, lock something else and then slew the TPOD to match the Maverick and re-designate on the TPOD.
  1. Press the BSGT OSB (only appears if Maverick is locked).
2. Repeat 4-6 for each station. (Press Flip-down Trigger to step to next station.)
Using TPOD to aim Mavericks, once boresighted -- WIP
Ensure Mavericks are set to PRE mode on SMS page.
  - May have to select different weapon, then Mavericks again, to be able to cycle PRE/VIS/BORE, or set SOI to WPN MFD and press Radar Cursor Enable button (shift TDC press)??
1. On Maverick MFD, missile station should show an S above it (for Slaved to TGP). If it doesn't, put SOI to Maverick MFD and press TMS down to unlock any target it might be tracking, or press Flip-down Trigger to change to next pylon which resets the missile.
2. Set TGP page as SOI and use Ministick to slew crosshairs to target. Maverick seeker should follow TGP crosshairs.
3. Press TMS up to make a point track and initiate the handoff to the Maverick. If in AUTO mode (shown on TGP page), Maverick will attempt a lock (only with IR Mavericks, not E/O). If in MAN mode, Maverick will be pointed at the target but you need to put SOI on the WPN page (Dish Hat down) and lock manually (TMS up).