1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

507a - A/G - AGM-88C HARMs without HTS pod (see next page for HTS)

Master Arm ... ON
Master Mode ... A/G
SMS page ... Select AG88 and PWR ON

(HARMs can be carried on stations 3, 4, 6, and 7, but in USAF service are only carried on stations 3 and 7.)

Missile can only search for 5 radar types at once. There are 3 "ALIC" Tables that can be set up with 5 radars each. Tables and emitter IDs are shown on HARM tables page. Defaults are:
- Table 1 - long range missiles: SA-10 and SA-11 radars
- Table 2 - short range missiles and guns: 2S6/SA-19, Tor/SA-15, SA-8, ZSU-23-4, and Dog Ear radar
- Table 3 - older missiles: SA-2, SA-3, SA-6, SA-13

To edit a table:
1. AG Master Mode
2. LIST button on UFC
3. 0 for MISC
4. 0 for HARM
5. Increment/Decrement switch to select table
6. Select ID field with Dobber switch up/down.
7. Type new ID on UFC keypad, then press ENTR.
8. When finished, press RTN on Dobber switch to return to main DED page.

Modes:
HAS mode - HARM As Sensor (uses the missile itself to target emitters, similar to F/A-18C; missile flies directly to target without lofting)
1. AG Master Mode, Master Arm ON, AG88 selected on SMS page.
2. On SMS page, PWR OFF OSB to power on the missiles.
3. On left MFD, go to WPN page and set it as SOI (Dish Hat down). Set up missile:
  1. Mode is shown on top row left, press that OSB until it shows HAS.
  2. Up to 10 emitters will be shown for current table. Press TBLn OSB to cycle tables, or TMS left short.
  3. Scan cycle can take up to 1m30s. Remove types from scan with SRCH OSB, unhighlight ones you don't want to search for, press HAS OSB to return to main page, then RS OSB to Reset Search scan.
  4. Press Flip-down trigger (or long??) or OSB at top to change scan FOV for faster scan times.
  5. Use TDC slew to select emitter, TMS up to lock/unlock. Handoff takes about 5 sec.
4. With emitter locked and handed off, fly toward it until FOV box at bottom of HUD is flashing.
5. Press Red Button to fire.

POS mode - Position (uses steerpoint at target to find range, missile lofts for longer range)
POS sub-modes:
- PB (Pre-Briefed) - Longest range, on-boresight, seeker activates at 15 nmi, 120 deg FOV
- EOM (Equations of Motion) - Medium range, off-boresight, seeker activates at 5 nmi, 40 deg FOV
- RUK (Range Unknown) - Shortest range, off-boresight, seeker activates at 20 nmi, 120 deg FOV
To use missile:
1. AG Master Mode, Master Arm ON, AG88 selected on SMS page.
2. Select steerpoint that is near the target.
3. On SMS page, PWR OFF OSB to power on the missiles.
4. On left MFD, go to WPN page and set it as SOI (Dish Hat down). Set up missile:
  1. Mode is shown on top row left, press that OSB until it shows POS.
  2. Sub-mode is shown on top row center, press that OSB to select sub-mode.
  3. Select the threat table you want to attack with TBLn OSB, or TMS left short.
  4. Press the OSB next to the specific threat you want to target at the steerpoint.
5. HUD shows some information:
Range scale on right. Top to bottom is:
  - Upper range scale number (40 or 80 nmi).
  - A caret showing current range to target.
  - A bracket/staple showing dynamic MMZ (Missile Maneuvering Zone). Changes depending on your speed and altitude.
  - A short horizontal line showing zero range.
Bottom of HUD:
An FOV box showing the final FOV area of the missile at the target??
1. Fly the plane toward the target. In RUK mode, you can only launch when the caret is in the MMZ. However, you can launch from off boresight.
2. When the FOV box is flashing, missile is in parameters, press Red Button to fire.
  - Top half of the WPN MFD page shows fired missiles (steerpoint on top, emitter type fired at on bottom).