202 - Ground - Preflight, Performance Limits

If using Auto Start from cold, check before proceeding:
1. Standby Attitude Indicator ... Uncage and set to same as primary
2. PITOT HEAT ... ON (front panel lower right)

Before takeoff (hot start or manually cold started)
1. RADAR knob ... STBY or OPER (must take off within 10 minutes to avoid overheating)
2. Altimeter ... Set to zero with pressure adjustment knob.
3. RWR ... ON
4. Radio ... MAIN or BOTH (monitors Guard)
5. CHAFF and FLARE knobs ... SINGLE (left console rear)
6. Fuel AUTO BALANCE switch ... LEFT LOW (front panel lower right)
7. Fuel EXT PYLON switches ... As needed (front panel lower right)
8. Pitch Trim ... As needed (dial, front panel upper left) (empty = 6 deg, gun/missiles/droptanks = 7 deg, that + bombs/rockets = 8 deg, max load = 9 deg)
9. Begin taxi.

Performance limits
- Fuel: 4511 lbs internal
  - 150 drop tank: 974 lbs (22% of internal)
  - 275 gal drop tank: 1775 lbs (39% of internal)
- 0 G or less: 9 sec at full power (more time if at less than full power, up to 60 seconds but nonlinear)
- Flaps: Automatic
- Landing Gear: 260 kts
- Rolling speed on ground: 230 kts
- Canopy open: 50 kts
- Descent rate on landing: <3700 lbs fuel = 600 fpm, >3700 lbs fuel = 360 fpm
- Max G with missiles only: +7.3/-3.0
- Max G with underwing stores: +6.5/-2.0
- Max G with underwing stores and underwing 275 gallon tanks: +4/-1.5