501 - A/G - Unguided Bombs, Rockets, LABS

Guns with radar ranging
Mechanical Sight ... Uncage
All other controls on center console between legs
1. Gun-Missile selector knob ... GUNS (Gray Reset Hat back)
2. Sight Function Selector lever (bottom lever on dial) ... GUN (Gray Reset Hat left/right)
3. Bomb-Target Wind Control knob ... ROCKET GUN (bottom of dial)
4. Press and hold Electrical Cage button (Front Thumb Button) and dive at target.
5. When pipper is on target, release Electrical Cage.
6. When in range (maybe 3000 ft or less??), fire with Trigger.

Rockets with radar ranging
1. If carrying rockets and droptanks, ensure Rocket Intervalometer Dial (left console rear) is set to 9 initially. If carrying rockets with no droptanks, dial should be set to 1 (default).
2. Mechanical Sight ... Uncage
All other controls on center console between legs
1. Gun-Missile selector knob ... SIGHT CAMERA & RADAR
2. Sight Function Selector lever (bottom lever on dial) ... ROCKET
3. Rocket Depression Angle lever (top lever on dial) ... As needed, approx 40 mils seems to work for a 20 to 30 deg dive
4. Rocket Release Selector switch ... As desired: Up for single rockets, Down for ripple while Red Button is held (red guarded switch, use B3 and B6 buttons to move the actual switch)
5. Bomb-Target Wind Control knob ... ROCKET GUN (bottom of dial)
6. Press and hold Electrical Cage button (Front Thumb Button) and dive at target.
7. When pipper is on target, release Electrical Cage and track target for about 3 seconds.
8. When in range (maybe 3000 ft or less??), fire with Red Button.

Bombs -- Common setup for all bombing
Mechanical Sight ... Uncage
All other controls on center console between legs
1. Rocket Release Selector switch ... OFF (middle position, or close switch guard)
2. Gun-Missile selector knob ... SIGHT CAMERA & RADAR (Gray Reset Hat press)
3. Loadout to Drop switch ... As needed (ALL, LEFT, or RIGHT)
4. Fuze Mode switch ... ARM NOSE & TAIL
5. Bomb-Target Wind Control knob ... As needed (when bombing into the wind, set wind speed in kts to the left of the 0; when bombing with the wind, set wind speed in kts to the right of the 0)

Dive bombing with automatic release
1. Sight Function Selector lever (bottom lever on dial) ... BOMB (Gray Reset Hat left/right)
2. Release Mode switch ... AUTO (automatic system can also be used in MANUAL mode: pipper will blink out when bombs should be released)
3. Start well away from the target, maybe 5 miles, and 10k ft minimum. For steeper dives, start at higher altitude. Starting dive at around 300 kts IAS seems to give best accuracy, but needs more testing.
4. Cut throttle and deploy airbrakes for maximum tracking time, hold Electrical Cage, and dive in.
5. Put pipper on target and hold it there.
6. When radar shows first flickers of ranging, release Electrical Cage and hold Red Button.
7. Continue to track target, pushing forward stick as needed, until bombs release.
  - Release altitude will usually be around 4k ft and 350 to 400 kts.

Dive bombing with Manual Pip (pipper) Control (MPC)
1. Sight Function Selector lever (bottom lever on dial) ... Gun (Gray Reset Hat left/right) (according to the real-life manual, GUN is used for MPC bombing)
2. Release Mode switch ... MANUAL
3. Determine target altitude above sea level, desired dive angle, and your initial altitude.
4. On MPC unit, set switch to BOMB.
5. Flip to the page for the altitude above the target you want to start your run. The page will also show the required dive entry speed. Higher starting altitude gives you more time for corrections.
6. Turn the knob on the MPC unit to your desired dive angle on the inner scale.
7. Read the "index altitude" for that angle from the outer scale. This is the altitude above the target that you'll drop.
8. On the Bombing Altimeter (left base of the gunsight):
  1. Set the "index altitude" using the long needle.
  2. Set the target altitude by turning the knob to move the red needle.
9. Fly the speed shown on the MPC card, at the altitude above the target shown on the MPC card. When you're ready to dive at the angle you've set:
  1. Quickly: Throttle to idle, speed brakes out, roll and dive on the target at the correct angle.
  2. Put pipper on the target and watch the bombing altimeter.
  3. When the white needles on the altimeter meet, release bomb with Red Button.
10. When finished, set the switch on the MPC unit to NORMAL.