1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

304 - Flight - Carrier Landing with ACLS

All carrier landings:
Set TACAN to carrier frequency so you can monitor direction and distance to carrier.

Case III recovery with ACLS (Automatic Carrier Landing System) -- WIP, needs verification
- NOTE: Carrier must be set up in the mission editor to support ACLS, see Wags video. ACLS is only available in CASE III conditions -- IFR conditions: <1000 ft ceiling or < 5 nmi visibility, or night.
- Mode 1 is completely hands-off automatic landing, Mode 1A is manual flying with all guidance cues, Mode 2 is manual flying with minimal guidance cues.
Within 50 miles of the carrier, call "Inbound" on radio. Carrier will respond with weather, altimeter setting, and BRC, and then will give marshal stack radial (bearing to the carrier), distance, assigned altitude, and expected push time (in minutes after the hour).
  - The marshal stack distance is 1 nmi for every 1000 ft of altitude, plus 15. So if you are assigned an altitude of 10000 ft, you should be at 10 + 15 = 25 nmi from the carrier.
  - Lowest position on the stack (and therefore next to proceed to landing) is 6000 ft at 21 nmi.
1. Set up systems:
  1. Set ICLS (UFC ILS button) to carrier frequency so you can fly the needles.
  2. Tune Link4 datalink (UFC D/L button 1x) to correct frequency (default is 336.0).
  3. On right MFD, go to HSI page, set HSI course line to carrier's BRC. (CRS switch on center console above center MFD.)
  4. On left MFD, go to HSI page, then press ACL OSB (L5 OSB).
  5. Top right of ACL page will show TEST as it tests the datalink handshake.
  - If link succeeds, top right of ACL page will say ACL 1. Proceed.
  - If it fails (UTM FAIL??), it means you have the wrong Link4 frequency or the mission editor isn't set up correctly. Tune correctly, then go back to the HSI page and ACL OSB again to re-do testing link.
1. When at correct altitude and within 20 miles of the marshal stack, radio "Established".
2. HUD will show flashing DATA label on right when ACL system is receiving new data. ACL page should now show CMD A/S (Commanded Airspeed), CMD ALT (Altitude), CMD ROD (Rate Of Descent), and T/C (Traffic Control mode); compass portion will show caret for marshal stack entry point??
3. Commence landing from marshal stack onto the final bearing (BRC). Call "Commencing".
4. HUD will show flashing DATA, ACL page CMD cues will be updated to show descent path, compass will show caret at bearing to carrier. Follow cues to begin descent.
5. When you pass 5000 ft descending, call "Platform".
6. HUD will show flashing DATA, ACL page CMD cues will be updated to show final descent path. Follow cues.
7. At 10 miles, gear down, flaps full down, check hook down.
8. At 8 miles, HUD will show flashing DATA, ACL page CMD cues will be updated. LND CHK reminds you to check landing configuration. Follow cues.
9. At 6 miles, engage ATC (autothrottle, Pinky Hat press). ACL page will say ACL RDY, MODE 1. HUD should show the "tadpole" guidance cue. (Velocity vector on tadpole will result in landing.)
10. You are currently in Mode 1A landing (manual flying with all guidance cues). Engage full Mode 1 landing (hands-off fully automatic) with A/P CPL mode (UFC A/P button, CPL OSB).
  - If you need to take manual control at any point, press Paddle Switch to disengage A/P CPL.
1. HUD should show CPL P/R (Coupled Pitch/Roll) and ATC (autothrottle engaged). Plane will intercept the glide slope and fly down to a OK 3-wire:
  1. At 4 miles, HUD will show flashing DATA, ACL page will say CMD CNT, MODE 1.
  2. At 3/4 mile, call the ball.
  3. Don't forget to go to mil power on touchdown.