1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

501 - A/G - Guns, Rockets

Master Arm ... ON
Master Mode ... A/G

Guns -- M61 Vulcan 20 mm, 578 rounds
1. On left MFD, go to STORES page.
2. Select GUN OSB.
3. Set pipper options:
  - CCIP OSB -- Uses CCIP pipper (default).
  - MAN OSB -- Set the pipper depression manually with UFC OSB (sets RTCL (reticle) value).
Set ammo type:
  - M50 OSB -- HEI-T, HEI, AP, TP (default load)
  - PGU OSB -- SAPHEI, TP PGU (must select this setting manually if using PGU ammo)
Set fire rate:
  - HI LO OSB -- Toggles fire rate between 6,000 rpm (HI, default) and 4,000 rpm (LO).
1. For best accuracy when using CCIP, press Dish Hat up to put SOI to HUD/HMD. That will turn on AGR (Air-Ground Ranging) radar mode, and radar will be used to get exact range to CCIP impact point.
2. Put CCIP dot on the target and press Trigger 2nd stage to fire gun.

Rockets
1. On left MFD, go to STORES page.
2. Select rockets (61 is 19-shot, 68 is 7-shot, 10 is Zuni, S is Single rocket per pickle press, R is Ripple while pickle is held; Single/Ripple is set up in the mission editor, cannot be changed in flight.)
3. Press CCIP OSB to use CCIP, or MAN OSB if you want to set the pipper depression manually.
4. Press SGL OSB to launch from one pod at a time, or SAL OSB to launch from all pods of the same type.
5. For MTR OSB (at bottom), leave at M66 (MTR is rocket motor type, documentation unclear, M66 seems to be default)
6. For best accuracy when using CCIP, press Dish Hat up to put SOI to HUD/HMD. That will turn on AGR (Air-Ground Ranging) radar mode, and radar will be used to get exact range to CCIP impact point.
7. Put CCIP dot on the target and press Red Button to fire rockets.