1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

502 - A/G - Unguided Bombs with CCIP

Master Arm ... ON
Master Mode ... A/G

CCIP bombing (special instructions for Mk 20 Rockeye/CBU 99 below)
All
1. On left MFD, go to STORES page.
2. Select unguided bombs.
3. Set options:
  - MODE ... AUTO (CCRP level or toss) or CCIP (FD is not implemented yet, MAN is when you set the pipper depression manually)
  - MFUZ ... use NOSE or NSTL for most bombs, but see below
  - EFUZ ... As desired (INST recommended for most bombs, but see below)
  - DRAG (if applicable) ... FF (Free Fall/slick) or RET (Retarded) as desired
To set ripple and interval, press UFC button. Then on the UFC itself:
  - QTY ... total number of release impulses
  - MULT ... number of bombs to be dropped per impulse
  - Total bombs dropped will be QTY x MULT.
  - INT ... interval spacing in ft
1. Put CCIP dot on the target and hold Red Button until all selected bombs are gone.
2. If there's a horizontal bar across the CCIP bomb fall line (longer than the impact crosshair line), that's the "reflected cue": actual impact point is off the bottom of the HUD. Unlike F-16 and AV-8B, holding pickle will not convert to a CCRP drop, you must either dive steeper or get to a lower altitude to make the reflected cue go away and enable bomb release.
3. For best accuracy when using CCIP, press Dish Hat up to put SOI to HUD/HMD. That will turn on AGR (Air-Ground Ranging) radar mode, and radar will be used to get exact range to CCIP impact point. When SOI is in HUD/HMD you can also press TDC press to designate a target (at VV, or HMD pipper), which will automatically switch you to CCRP mode.
Mk 20/CBU 99 Rockeye
- Buttons on SMS page:
  - MFUZ
    - PRI -- Bombs will burst 1.2 seconds after release
    - VT -- Bombs will burst at 1500 ft AGL (hardcoded), or 1.2 seconds after release, whichever is later
  - With MFUZ in VT, press HT OSB to cycle through burst heights (shown in columns of data in the center). Set to 1500 to match hardcoded burst height. Other burst heights may be implemented in the future, but the HT setting here is for release symbology, NOT for setting the actual burst height.
- For level release, put target just below bottom of CCIP cross line. For release in near-vertical dive, use CCIP aimpoint. For angles between these, adjust proportionally: steeper angle is closer to center of CCIP crosshair.
- Pattern is determined by flight angle. Very steep dive (75 deg) results in a tight pattern, level release results in a longer pattern. Longer patterns may fall short, so aim long if doing a level release. A single Mk 20 can kill a tank if you get lucky.

CCRP bombing
All
1. Designate a target, either from a waypoint (WPDSG OSB on HSI or SA page), with TPOD (see other checklist), on A/G radar, or visually:
  1. Press Dish Hat up to put SOI in HUD. Shows "Ball and Chain" symbology.
  2. Put Ball and Chain pipper on target, or look at target with HMD, and press TDC press to designate. Then adjust target diamond with TDC slew if needed.
2. Once you have a target, fly toward the bomb fall line.
3. HUD shows xx REL countdown to release time, and xx.x TGT distance to target.
4. Release cue line falls from top of bomb fall line toward VV. Hold Red Button until all bombs drop.

Toss/loft bombing from low level
1. Follow CCRP bombing steps above to set up attack.
2. At the desired time until target (see table, 20 seconds recommended), hold pickle and pull up sharply to the Stabilize angle, then stop pulling and stabilize in a steady climb.
  - IMPORTANT: You need to be stabilized at the moment of bomb release or accuracy could be poor or all bombs may not drop.
1. Release cue line (horizontal line) should almost immediately appear coming down the vertical bomb fall line. Bombs will release when the release cue reaches the velocity vector.
2. As soon as the bombs are gone, pull hard up and over until partly inverted and get back down to low altitude. The HSI/SA page has a reciprocal marking for the target heading.
Pull up time	Pull up distance	Stabilize angle	Release angle	Release alt	Max aircraft alt	Closest approach	Exposure time
15 sec	3.0 nmi	15 deg	~15-20 deg	500-1000 ft	2000 ft	1.8 nmi	15-20 sec
20 sec	3.75-4.0 nmi	20 deg	~20-25 deg	1000 ft	2500 ft	2.5 nmi	20 sec
25 sec	4.5 nmi	30 deg	~30-35 deg	1500-2000 ft	3500-4000 ft	3.25 nmi	20 sec