1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

503 - A/G - Unguided Bombs with CCRP and Toss/Loft bombing

Master Arm ... ON
Master Mode ... A/G

CCRP bombing
1. On left MFD, go to STORES page.
2. Select unguided bombs.
3. Set options:
  1. MODE ... AUTO
  2. MFUZ ... use NOSE or NSTL for most bombs, but see below
  3. EFUZ ... As desired (INST recommended for most bombs, but see below)
  4. DRAG (if applicable) ... FF (Free Fall/slick) or RET (Retarded) as desired
4. To set ripple and interval, press UFC button. Then on the UFC itself:
  1. QTY ... total number of release impulses
  2. MULT ... number of bombs to be dropped per impulse
  3. Total bombs dropped will be QTY x MULT.
  4. INT ... interval spacing in ft
5. Designate a target, either from a waypoint (WPDSG OSB on HSI or SA page), with TPOD (see other checklist), on A/G radar, or visually.
6. Once you have a target, fly toward the bomb fall line.
7. HUD shows xx REL countdown to release time, and xx.x TGT distance to target.
8. Release cue line falls from top of bomb fall line toward velocity vector. Hold Red Button until all bombs drop.

Toss/loft bombing from low level
1. Follow CCRP bombing steps above to set up attack.
2. At the desired time until target (see table, 20 seconds recommended), hold pickle and pull up sharply to the Stabilize angle, then stop pulling and stabilize in a steady climb.
  - IMPORTANT: You need to be stabilized at the moment of bomb release or accuracy could be poor or all bombs may not drop.
1. Release cue line (horizontal line) should almost immediately appear coming down the vertical bomb fall line. Bombs will release when the release cue reaches the velocity vector.
2. As soon as the bombs are gone, pull hard up and over until partly inverted and get back down to low altitude. The HSI/SA page has a reciprocal marking for the target heading.
Pull up time	Pull up distance	Stabilize angle	Release angle	Release alt	Max aircraft alt	Closest approach	Exposure time
15 sec	3.0 nmi	15 deg	~15-20 deg	500-1000 ft	2000 ft	1.8 nmi	15-20 sec
20 sec	3.75-4.0 nmi	20 deg	~20-25 deg	1000 ft	2500 ft	2.5 nmi	20 sec
25 sec	4.5 nmi	30 deg	~30-35 deg	1500-2000 ft	3500-4000 ft	3.25 nmi	20 sec