1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

504 - A/G - TPOD

Master Arm ... ON
Master Mode ... A/G

TPOD use
1. These steps are for the LANTIRN, but are basically the same for the ATFLIR as well.
2. Set SOI to FLIR MFD (Dish Hat toward MFD once). Special notes about tracking modes:
  - If you press Dish Hat toward the MFD when it's already SOI, it will cycle between Ground-stabilized, Area track, and Point track modes. Only ground-stabilized can be slewed.
  - Mode is shown in upper left corner of MFD. OPR only is ground-stabilized, OPR / ATRK is Area Track, OPR / PTRK is Point Track (used for moving targets). If you are in a ATRK or PTRK, the diamond target marker shown in the HUD or HMD will be solid, otherwise it will be dashed.
  - Track is not necessary for designating target.
  - If in ATRK or PTRK mode, you cannot slew the crosshairs.
  - If you get stuck in a mode, reset by pressing Flip-down Trigger until it undesignates and slaves to Velocity Vector (VVSLAV). If you get really stuck, set FLIR switch to STBY and then back ON.
1. On FLIR page, press VVSLAV button or double-press Flip-down Trigger to slave pod to Velocity Vector.
2. Press TDC press to Ground-stabilize the pod. Can be done even if VV is above the horizon.
3. Once Ground-stabilized, use TDC slew to move crosshairs. (If you can't slew, press Dish Hat toward FLIR MFD to cycle mode until you get back to ground-stabilized.)
4. Press Pinky Button or WIDE/NAR OSB to toggle wide/narrow view.
5. Middle-finger Hat up/down to zoom out/in (additional zoom to wide/narrow).
6. Long-press Pinky Button (or press MFD button) to toggle CCD/FLIR mode.
  - In FLIR mode, press MFD BLK or WHT button to toggle black-hot/white-hot, press ALG button to toggle automatic or manual gain control (ALG boxed is automatic gain). In manual gain, buttons on left side of MFD can be used to set gain and contrast.
1. Crosshairs move more slowly when zoomed in; to slew quickly, zoom out and/or set wide view.
2. Max visibility range is 40 nmi due to graphics rendering distance. Max laser range is at least 15.6 nmi.
Using HMD or visual designation with TPOD
  1. If you have a target designated, designation point will show as a dotted diamond in HMD.
  2. You can slew the designation either visually by setting SOI to HUD/HMD (Dish Hat up), or with the SOI on the TPOD MFD as usual.
  3. If you have no target designated yet, pressing Dish Hat up will put SOI in HUD/HMD and shows "Ball and Chain" symbology.
  4. Put Ball and Chain pipper on target, or look at target with HMD, and press TDC press to designate. Then adjust target diamond with TDC slew if needed.
  5. IMPORTANT: Press Dish Hat right to put SOI back to TPOD MFD. If you leave SOI in the HUD/HMD, slewing will be way too fast on the TPOD MFD.

Valid laser codes:
Format is ABCC, A=1, B=1-7, C=1-8, never 0 or 9. Range should be 1111 to 1788. Some planes in DCS (A-10C?) may not be able to set B=7.