1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

506 - A/G - GBU-24 Paveway III

Master Arm ... ON
Master Mode ... A/G

GBU-24 Paveway III with TPOD
Optimum range is about 5.8 nmi from 20,000 ft at 0.85 Mach, may be able to go further with CLAR OVD (see step 9), but needs testing. GBU-10 max range is 4.8 nmi from same altitude and speed.
1. Go to STORES page (left MFD):
  1. Select bombs (GBU-24)
  2. MODE button:
    1. CLAR PP (Pre-Planned) -- Adds symbology for flying a planned attack direction.
    2. CLAR SL (Straight Line attack) -- Symbology assuming you will be flying directly at the target.
    3. MAN -- Unknown??
    - CLAR = Computed Launch Acceptable Region, the symbology that shows the drop zone.
  1. MFUZ button ... TAIL for delay/penetration fuze, N/T for no delay.
  2. Set laser code on bombs ... Press CODE button on MFD, press CODE button on UFC, enter code on UFC, press ENT.
  3. Press STEP button to go through the pylons and set all codes.
  4. If using CLAR PP, set planned attack heading by pressing UFC OSB, then select HDG button on UFC and enter heading.
  5. CLAR OVD -- If boxed, your pickle is immediately hot and you can drop the bomb outside the LAR. Automatic lasing is disabled! You must select TRIG on the FLIR and lase manually with trigger 2nd stage.
2. LTD/R switch ... ARM (on right hand console) (or throttle T4 switch)
3. Go to FLIR page (right MFD) and set laser code on TPOD:
  1. Press UFC button on right of MFD (near CODE/1688) (laser must be in ARM for this to show).
  2. Press LTDC on UFC itself (must be in A/G Master Mode for this to show).
  3. Enter code on UFC keypad, press ENT.
  - (LST and LSTC are for the Laser Spot Tracker; it can have same or different code, doesn't matter)
1. Designate target with TPOD (see steps on other checklist).
2. Bomb fall line will initially be a dashed line, with short horizontal lines above and below VV showing optimal min/max release ranges. HSI page (not SA page) also shows a box that is the optimal release zone.
3. Fly toward bomb fall line.
4. When bomb fall line is in the HUD, HUD will show xx TMR count down to Time to Maximum Range.
5. Bomb drop cue is a dot falling down the bomb fall line. When dot is between horizontal min/max lines, bomb fall line will become solid. Bomb will drop when dot reaches VV, about halfway between the min and max range.
6. A few seconds before release, hold pickle until bomb drops.
  - You can also drop at any time by pressing CLAR OVD OSB on STORES page, which will make the bomb fall line solid immediately and make your pickle hot.
1. HUD will show xx TTI countdown to Time To Impact.
2. You can adjust the crosshairs on TPOD as needed before bomb impacts.

Valid laser codes:
Format is ABCC, A=1, B=1-7 (or 1-6 in DCS??), C=1-8, never 0 or 9. Range should be 1111 to 1788 but may be 1111 to 1688 in the game. Some planes in DCS (A-10C?) may not be able to set B=7.