1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

507 - A/G - JDAM, JSOW

Master Arm ... ON
Master Mode ... A/G

JDAM and JSOW -- Basically the same, but JSOW has longer range
TOO mode (regular target designation using tpod, A/G radar, HMD, waypoint designate, etc)
1. Go to STORES page (left MFD) and set up weapon:
  1. Select weapons. Once selected, the JDAM/JSOW starts aligning, which can take up to 8 minutes. DO NOT UNSELECT THEM or they will lose alignment. Some other weapons like HARMs and Mavericks can be selected at the same time.
  2. Press MODE PP OSB to change to MODE TOO. MODE is per pylon. Recommended to press STEP OSB and set MODE TOO for each pylon.
  3. EFUZ ... As desired
2. Press JDAM DSPLY OSB on STORES page:
    1. REL TYPE ... MAN (default, LOFT and FD (Flight Director) not implemented yet)
    2. QTY ... As desired (all bombs released in the same release pulse will go to the same target)
3. Press MSN OSB on JDAM DSPLY page to go to mission setup page:
  1. Press TOO UFC OSB to set terminal attack parameters on UFC (may not be fully implemented, LAR may not take terminal settings into account??):
    1. HDG -- Heading of bomb at time of impact, 0 to 359 deg (press HDG UNDF OSB to reset)
    2. ANG -- Impact angle of bomb, 0 to 90 deg.
    3. VEL -- Velocity at impact, 100 to 26800 feet per second.
4. Designate target with tpod (see steps on other page) or other method.
5. When IN ZONE, hold Red Button to drop bomb.
  - If attacking multiple targets, slew tpod to next target, press TDC press to designate new target, press Red Button again.
1. You can see the LAR (Launch Acceptable Region/drop zone) in the HSI page (not SA page).
2. Accuracy may be affected by max range, try to drop nearer to the middle of the LAR.
PP mode (entering coordinates directly into the bombs so you can drop them without a designated target)
1. Follow steps above to step 3, but set MODE PP (default) instead of TOO. Then on the MSN page:
  1. Box PP1 OSB (will be crossed out) to set up the first target point.
  2. Press TGT OSB to set target position and terminal parameters on UFC (press TGT OSB again to return to this UFC menu):
    1. TERM -- Terminal attack parameters (may not be fully implemented, LAR may not take terminal settings into account??):
      1. HDG -- Heading of bomb at time of impact, 0 to 359 deg (press HDG UNDF OSB to reset)
      2. ANG -- Impact angle of bomb, 0 to 90 deg.
      3. VEL -- Velocity at impact, 100 to 26800 feet per second.
    2. POSN -- LAT and LONG as DDMMSS, enter, decimal SS, enter
    3. ELEV -- feet or meters
  3. After all parameters are valid, PP1 should not be crossed out. Target is now valid and HUD displays countdown to in-range.
2. When IN ZONE, hold pickle to drop bomb.
3. You can see the LAR (Launch Acceptable Region/drop zone) in the HSI page (not SA page).
4. Accuracy may be affected by max range, try to drop nearer to the middle of the LAR.

JDAM toss/loft attack -- WIP
Wait until almost IN RANGE before pulling, at most 5 seconds away. IN RANGE cue should appear when still a good distance away (~5 nmi??). Pull up to around 15-25 deg and pickle. As long as you're IN ZONE the exact release parameters don't matter much.