1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

508 - A/G - AGM-84E SLAM, AGM-84K SLAM-ER

Master Arm ... ON
Master Mode ... A/G

AGM-84E SLAM -- 1000 lb warhead, range approx 67 nmi, speed approx 480 kts at 5000 ft
TOO mode without AWW-13 datalink pod (GPS guidance only, does not use the IR seeker)
STORES page, SLAM OSB. Takes 2m30s to warm up, shows RDY under SLAM OSB when warmed up.
  - GPS will also begin aligning when SLAM is boxed, should get to ALN QUAL 01 GOOD.
  - Deselecting SLAM OSB will power-down missile; will go through warm-up cycle again if re-selected.
Set missile options:
  - MODE PP OSB (per missile) to change to MODE TOO.
  - FLT OSB (per missile) to change cruise altitude (altitude is shown on bottom left):
    - HIGH	- 35,000 ft
    - MED	- 15,000 ft (default)
    - LOW	- 5,000 ft
  - EFUZ OSB (all missiles) to toggle OFF/INST fuzing (fuzing is shown on bottom left).
  - STP OSB (per missile??), when boxed, will use the currently selected waypoint or markpoint as a course waypoint for the missile. If unboxed, missile will fly straight in with no course changes.
1. Designate a target (WPDSG, TPOD, etc.). Target must be designated while SLAM is selected and warmed up in order for it to register with the missile.
2. Set additional options in SLAM DSPLY OSB page:
  - REL TYPE OSB - Only use MAN, other options not implemented.
  - MSN OSB opens another page with more options:
    - HDG UNDF OSB	- Clears terminal impact heading (see TOO UFC OSB below)
    - TOO UFC OSB	- Sets terminal impact options on UFC:
      - HDG	- Missile heading at impact (0-359, clear with HDG UNDEF OSB)
      - ANG	- Dive angle at impact (0-90 deg, 0 is default)
      - VEL	- Missile velocity at impact in ft/sec (100-26800, 0 is default)
    - O/S UFC OSB	- Something to do with offset aimpoints...?? Probably not important.
1. TMR countdown on HUD and STORES page shows Time to Max Range. HSI page (not SA page) also shows circles for weapon max and min ranges.
2. When in range, press Red Button to launch.
TOO mode with AWW-13 datalink pod (man-in-the-loop guidance using IR seeker)
1. On left MFD, go to STORES page, press DL13 OSB.
2. Follow steps 1-4 above to select, warmup, and configure missile.
3. Once missile is set up, press WEP OSB to pair a missile with the datalink pod. Left side SLAM OSBs from top to bottom are station 2, 3, 7, 8. When paired, SLAM appears under DL13 OSB at top.
4. When missile gets close to the target, seeker automatically turns on and begins transmitting over the datalink. Default distance is 10 nmi (shown in bottom left of STORES page). Change the distance with SLAM DSPLY OSB page, then UFC OSB.
5. TTS countdown will show Time To Seeker activation.
6. TMR countdown on HUD and STORES page shows Time to Max Range. HSI page (not SA page) also shows circles for weapon max and min ranges.
7. When in range, press Red Button to launch.
8. When TTS reaches zero, STORES page should automatically show the seeker view. It's a modified Maverick seeker, you should see the same symbology: plus sign indicates where seeker is pointing relative to the missile. Toggle FOV with Pinky Button or FOV OSB, move TDC to slew seeker to new target. Datalink quality decreases with range.
  - WARNING: TDC moves the seeker designator, does not fly the missile directly like the Walleye. Missile does not start maneuvering until new target is locked (TDC stops slewing). Pick a target early and let the missile fly itself in.
PP mode
TODO -- Should be almost the same as TOO mode, except you need to manually enter the target coordinates into the missile via the STORES > SLAM DSPLY > MSN page.

AGM-84K SLAM-ER -- 1000 lb warhead, range approx 146 nmi, speed approx 500 kts at 5000 ft
Identical in use to the AGM-84E SLAM except:
  - Much longer range, 146 nmi.
  - Better quality seeker head. When using seeker with datalink:
    - Seeker shows slant range to designated target, and tracking mode (F/C or CENT, see below).
    - Seeker crosshairs can be slewed freely without maneuvering missile. Must press TDC press to designate new target.
    - BLK OSB or WHT OSB toggles tracking Black or White objects respectively.
    - F/C OSB, when boxed, uses Force Correlate tracking (best for pinpointing parts of large buildings), when not boxed uses Centroid tracking (best for small targets or moving vehicles).
  - Can set up to 5 steerpoints for the missile to follow in sequence: STORES page > STP OSB, then on UFC select STP1, enter waypoint or coordinates, STP2, etc.