1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

509 - A/G - AGM-62 Walleye

Master Arm ... ON
Master Mode ... A/G

Recommended parameters: range 12 nmi at 20,000 ft, 18 nmi at 30,000 ft
Seeker head is optical, not IR. 2000 lb linear shaped charge warhead.

AGM-62 Walleye II with AAW-13 datalink pod (fire-and-forget or man-in-the-loop guidance)
1. On left MFD, go to STORES page, press WEDL OSB. It will be boxed and crossed out (because no target locked yet).
2. Note which station the selected Walleye is on (default is station 8).
3. Press WEDL OSB again and you should see the Walleye video feed.
  - NOTE: Walleye may take up to 3 minutes to warm up. If you don't see the video feed, wait.
1. Press INST OSB for instantaneous fuzing, or DLY OSB for delay fuzing. This must be done before activating the datalink (next step).
2. Press DL13 OSB. Now both it and WEDL will be boxed.
3. Top left corner of the MFD should say RDY STA 8 (or 2). This means the datalink is not paired to the selected weapon station.
4. Pair the datalink pod with the weapon:
  1. Press WPN OSB, then on the left side press one of the WEDL OSBs. Top one is Station 2 and bottom one is Station 8. Select the station that was active in step 2.
  2. When done, MFD should say RDY WEDL. This means you're seeing the feed through the datalink.
5. Set SOI to left MFD with video feed.
6. Press Cage/Uncage button (Rear Thumb Button) to uncage Walleye seeker.
  - If you have a designated target, the seeker will automatically slew to the target and you will not be able to slew the crosshairs manually.
  - To allow manual slewing, undesignate the target with Flip Down Trigger press. The Walleye seeker will remain pointed at the same place, but now you can slew it manually.
1. Press and hold TDC press while moving TDC stick to slew. Release TDC press to attempt contrast lock. When locked, WEDL will no longer be crossed out. Lock is not required when using datalink pod.
2. HUD gives TTMR (Time To Max Range) countdown. When in range, press Red Button to drop.
3. While bomb is falling, use TDC stick to guide it or change target lock. Walleye does not glide well and loses energy quickly, so don't maneuver too much. Recommended to get contrast lock as far out as possible and then don't touch it.
  - Walleye may overshoot target. Watch the white box and make sure it will be centered and hidden behind the center crosshairs at impact. You may need to steer it manually down to compensate.
1. Press the A ANT OSB to use the aft antenna on the AWW-13 if you're flying away from the target.
2. Datalink video quality gets worse with distance and when not facing the weapon with the selected antenna.

AGM-62 Walleye II without AAW-13 datalink pod (fire-and-forget)
1. On left MFD, go to STORES page, press WEDL OSB. It will be boxed and crossed out.
2. Press WEDL OSB again to show Walleye video feed.
  - NOTE: Walleye may take up to 3 minutes to warm up. If you don't see the video feed, wait.
1. Press INST OSB for instantaneous fuzing, or DLY OSB for delay fuzing.
2. Set SOI to MFD with video feed.
3. Press Cage/Uncage button (Rear Thumb Button) to uncage Walleye seeker.
  1. If you have a designated target, the seeker will automatically slew to the target and you will not be able to slew the crosshairs manually.
  2. To allow manual slewing, undesignate the target with Flip Down Trigger press. The Walleye seeker will remain pointed at the same place, but now you can slew it manually.
  - To re-cage, press and hold CRAB OSB (Caging Retention And Boresight) until it says CAGED in top right.
1. Press and hold TDC press while moving TDC stick to slew. Release TDC press to attempt lock. When locked, WEDL will no longer be crossed out.
2. HUD gives TTMR (Time To Max Range) countdown. When in range, press Red Button to drop.