1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

510 - A/G - AGM-65 Maverick

Master Arm ... ON
Master Mode ... A/G

- AGM-65E - Laser seeker, large warhead
- AGM-65F - IR seeker, large warhead
- My mnemonic: E for LasEr, F for inFrared

AGM-65F Mavericks (IR guided) -- WIP
Using Maverick seeker for targeting:
1. On left MFD, go to STORES page, select MAVF OSB. They take 3 minutes to cool down.
2. Press the MAVF OSB again to show the seeker video in the MFD.
3. Press Dish Hat left to put SOI to left MFD.
4. Press Uncage button to uncage the seeker.
5. Use TDC slew to put crosshairs on target. Press TDC press to attempt lock.
6. Once locked, press and hold Red Button to fire.
  - Maverick seeker "keyhole" is a circle about the radius of the second hashmark down, and a vertical section extending down to the third hashmark. Target must be within the keyhole for the missile to guide.
Using TPOD, radar, or visual targeting
1. On left MFD, go to STORES page, select MAVF OSB. They take 3 minutes to cool down.
2. Press the MAVF OSB again to show the seeker video in the MFD.
3. Designate a target either with the TPOD, radar, or visually.
  - To designate a target in GMT radar, put TDC cursor over target, then press Dish Hat Switch right (or toward radar MFD). If you press TDC press, you'll get a radar ground lock, not a target lock.
1. Maverick may override the Pinky Button's functions in the TPOD, even if it's not SOI.
2. Press Dish Hat left to put SOI to left MFD.
3. Press Uncage to uncage the seeker. It should automatically point at the designated target. You cannot manually slew the seeker in this mode. To enable slewing, press Undesignate to undesignate the target, then you can slew the crosshairs.
  - If it didn't lock onto the right target, press Cage/Uncage a couple times to cycle the missile and make it try locking the intended target again.
Once locked, press and hold Red Button to fire.
  - Maverick seeker "keyhole" is a circle about the radius of the second hashmark down, and a vertical section extending down to the third hashmark. Target must be within the keyhole for the missile to guide.

AGM-65E Mavericks (Laser guided)
Using TPOD for targeting:
1. On left MFD, go to STORES page, select MAV OSB. They take 30 seconds to warm up.
2. Press the MAV OSB again to show the seeker display in the MFD.
3. Press UFC OSB and set the laser code with the UFC keypad.
4. Designate a target with the TPOD.
5. Set SOI back to the MAV MFD and press Uncage to uncage the seeker. It should see the laser, shown with an X in the display.
  - Laser should fire automatically.
When IN RNG cue appears, press and hold Red Button to fire.
  - Target must be within the outer circle shown on the Maverick MFD for the missile to guide.