1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

511a - A/G - AGM-88 HARM

Master Arm ... ON
Master Mode ... A/G

AGM-88 HARM -- TODO: Test range at different altitudes.
HARMs fly in a straight line slightly downwards for several seconds after launch before starting to guide.

TOO (Target Of Opportunity) mode -- No loft
1. (Optional, but useful) On right MFD, go to EW page.
2. On left MFD, go to STORES page, select HARM.
3. Press TOO OSB.
4. HARM page shows emitters as seen out the front of the missile (azimuth/elevation view).
5. (Optional) Press CLASS OSB, then HOS OSB to show only hostile emitters, or other emitter classes.
6. Press Dish Hat left to put SOI to HARM MFD.
7. Press Pinky Button to cycle HARM target through all targets shown on HARM page. Target box is also shown on HUD, which can be used to point TPOD to do a visual search for the SAM site.
8. Press Uncage button to lock target ("hand-off", shows H-OFF under target box). All other targets are hidden when in H-OFF, this allows you to confirm your target. If needed, press Uncage again to un-hand-off to select a different target.
9. Press Red Button to fire missile at target.

SP (Self-Protection) mode -- No loft
1. (Optional, but useful) On right MFD, go to EW page.
2. On left MFD, go to STORES page, select HARM.
3. Press SP OSB.
4. Press Pinky Button to cycle HARM target through all targets shown on RWR.
5. Press Red Button to fire missile at target, no hand-off needed.
6. HARMs can even be fired "over the shoulder" at targets to the side or even behind, but firing envelope is limited since HARMs don't turn very fast.

PB (Pre-Briefed) mode -- Loft
1. On left MFD, go to STORES page, select HARM.
2. Press PB OSB.
3. Press UFC OSB.
4. On UFC, press TGT OSB, enter emitter ID (see HARM tables page), then ENT.
5. Select PULLUP option: A/C or HRM OSB. A/C is for lofting by pulling the aircraft up to a high pitch angle, HRM does the loft with the missile only.
6. Designate a target where you want the missile to go. Can be a waypoint (WP DSG OSB on HSI or SA page), or a regular target designation with TPOD or any other means.
7. STORES page shows missile flight times to the current target: 1st line for time if launched now, 2nd line for missile currently in flight. RNG will be crossed out if not in range.
8. HUD symbology shows Azimuth Steering Line, pitch-up carets, release line (horizontal line), and RNG.
9. Fly directly at the target. When RNG is not crossed out, press and hold Red Button and pitch up. When VV reaches release line (A/C loft, usually about 35 deg) or pitch-up carets (HRM loft), missile will fire.

HRM OVRD and Self-protect pullback
- When you're carrying HARMs, if you're locked up by a radar, the HARM will be automatically targeted at whatever is locking you.
- If HRM OVRD is boxed, HUD will show PLBK when you are locked on to, and pressing the pickle will show HARM crossed out, as the automatic self-protect has been overridden.
- If HRM OVRD is not boxed, HUD will show HARM (not crossed out) when you are locked on to by enemy radar, and pressing Red Button will fire a HARM at that emitter, regardless of what other weapon you have selected.
- If you're locked on by multiple radars, press Pinky Button press to cycle the HARM target, or Uncage button (Rear Thumb Button) to reset target to the highest priority emitter.