1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

512 - A/G - AGM-84D Harpoon

Master Arm ... ON
Master Mode ... A/G

AGM-84D Harpoon -- 500 lb warhead, range approx ??, speed approx ?? -- WIP, steps unverified
1. On left MFD, go to STORES page, select HPD. Alignment takes 25 seconds.
2. Set up missile options for each missile independently:
  1. MODE OSB, delivery mode:
    1. BOL - Bearing Only Launch, no target designation needed
    2. R/BL - Range / Bearing Launch, requires target designation to enable MODE OSB to switch to this
  2. FLT OSB, cruise altitude:
    1. HIGH - 35000 ft, max range and seeker area
    2. MED - 15000 ft
    3. LOW - 5000 ft
  3. TERM OSB, terminal attack behavior:
    1. SKIM - After acquiring target, missile flies at 25 ft altitude all the way to impact.
    2. POP - After acquiring target, missile does pop-up attack beginning at 5 nmi, up to 500 ft.
  4. SEEK OSB, seeker activation distance (R/BL mode only):
    1. SML - 10 km (5.4 nmi)
    2. MED - 20 km (10.8 nmi)
    3. LRG - 30 km (16.2 nmi)
      1. LEFT, RIGHT, NORM, NEAR, FAR??
  5. HPTP OSB, Harpoon Turn-Point:
    1. When boxed, HPTP sets current waypoint/markpoint (via HSI) as a dogleg point for the missile. If using BOL mode, distance is relative to HPTP instead of ownship. To change to a different waypoint, unbox, change waypoint, then re-box.
  6. FXP OSB, Fixed-Point (BOL mode only, cannot be used with HPTP):
    1. Sets a point halfway between Search and Destruct ranges for Harpoon search pattern??
  7. PROG OSB, cycles between 5 saved sets of settings.
  8. UFC OSB, additional options on UFC:
    1. SRCH (BOL mode only) - Range from launch point or HPTP that missile will begin active search. 0 to 105 nmi.
    2. DSTR - Range when missile will self-destruct, SRCH range to 172 nmi.
    3. BRG (BOL mode only) - Bearing relative to ownship or HPTP that missile will fly. Not used with FXP option.
  9. HSI page will show symbology for Harpoon missile path and waypoints as they're set up. Line indicates flight path, dot on line indicates HPTP, short cross-line is begin search point, X is self-destruct.
3. Minimum launch altitude is 2500 ft.
4. If using R/BL, fly toward target designator on HUD. When HUD shows IN RNG, fire with Red Button.
5. After launching, turn away to clear missile flight path in case it climbs.