304 - Flight - Carrier Landing

All carrier landings:
Set TACAN to carrier frequency so you can monitor direction and distance to carrier.

Case I recovery -- VFR conditions: > 3000 ft ceiling and > 5 nmi visibility
1. Within 50 miles of the carrier, call "Inbound" on radio. Carrier will respond with weather, altimeter setting, and BRC, ending with "Report see me at 10".
2. Fly directly to the carrier and enter the marshal stack. Be at correct altitude by 10 nmi.
  1. Marshal stack is a 5 nmi left hand circle, starting over the carrier and extending to the left for a 5 nmi diameter. Altitude is in 1000 ft increments starting at 2000 ft.
  2. "Point 1" is directly over the carrier, "Point 2" is ahead of the carrier, "Point 3" is abeam the carrier at 5 nmi to port, "Point 4" is aft of the carrier. Climb in the forward semicircle (Point 1 -> 2 -> 3). Descend in the aft semicircle (Point 3 -> 4 -> 1)
3. At 10 nmi with visual on the carrier, call "See you at ten", carrier responds "Update state, go tower", or "Update state, your signal is Charlie".
4. At 3 nmi from the carrier and with enough separation from other flights, you will automatically radio "<plane number> overhead..."??
5. When you have "Charlie", depart from the pattern at Point 3 (abeam the carrier at 5 nmi, heading aft).
6. Descend to 800 ft and maintain. When 3 nmi aft of the carrier, turn toward it so you'll pass outboard from the starboard side of the carrier.
7. Radio "Kiss off" to your flight when passing the carrier and execute overhead break turn to the left. (Allow 15 to 20 seconds between breaks to give 40 to 60 second intervals when landing.)
8. When established on downwind leg, descend to 600 ft and configure for landing. You should pass about 1.5 to 1.75 nmi from the carrier as you go past on the downwind.
9. Do a descending turn to roll out 3/4 nmi from the carrier "in the groove", then Call The Ball.
10. If you cannot see the ball, call "Clara" and LSO will guide to the glidepath.
11. Fly the ball down to an OK 3-wire.
Waveof‌f or bolter
1. Once off the deck and airborne again, turn right to BRC heading.
2. Climb to pattern altitude (600 ft) and turn downwind with proper spacing for other aircraft in the pattern.

Case II recovery -- intermediate conditions: > 1000 ft ceiling and > 5 nmi visibility
1. Set ILCS to carrier frequency so you can fly the needles.
2. Follow Case III recovery instructions below to step 5, where you will stop descending at 1200 ft.
3. At 10 nmi from the carrier, you should automatically radio "See you at 10".
4. Follow Case I recovery instructions above starting at step 4.

Case III recovery -- IFR conditions: < 1000 ft ceiling or < 5 nmi visibility, or night
1. Set ICLS to carrier frequency so you can fly the needles.
2. Within 50 miles of the carrier, call "Inbound" on radio. Carrier will respond with weather, altimeter setting, and BRC, and then will give marshal stack radial (bearing to the carrier), distance, assigned altitude, and expected push time (in minutes after the hour).
  - The marshal stack distance is 1 nmi for every 1000 ft of altitude, plus 15. So if you are assigned an altitude of 10000 ft, you should be at 10 + 15 = 25 nmi from the carrier.
  - Lowest position on the stack (and therefore next to proceed to landing) is 6000 ft at 21 nmi.
1. When at correct altitude and within 20 miles of the marshal stack, radio "Established".
2. Fly your holding pattern at assigned altitude and distance with 6-minute left hand turns: 2-minute turns and 1-minute legs.
3. Time your turns so you will be at the end of a leg going toward the carrier exactly at your push time.
4. At your assigned push time, radio "Commencing".
5. Descend at 4000 ft/min and 250 kts until 5000 ft altitude, then reduce descent rate to 2000 ft/min.
  1. As you are descending, carrier will call "Switch Approach", respond with "Check In".
  2. At 5000 ft altitude, radio "Platform". (Refers to passing "platform altitude" which is 5000 ft.)
  3. Level off at 1200 ft.
6. When you intercept the final landing bearing, carrier will radio "Fly bullseye", which means you should fly the ICLS needles.
7. At 10 nmi from carrier, begin reducing speed. At 8 nmi, configure for landing. At 6 nmi, be on-speed.
8. Laser lineup system light will be steady amber when lined up, flashing green if you're too far right, flashing red if you're too far left.
9. At 3/4 mile carrier will tell you to call the ball. Call The Ball, or call Clara if you can't see the ball.
10. Fly the needles and visually down to an OK 3-wire.
Waveof‌f or bolter
1. Climb to 1200 ft, raise gear to save fuel but leave flaps and hook down.
2. When instructed by Approach, turn downwind.
3. Inform carrier of fuel state when abeam.
4. Expect a turn back onto final when 4-8 nmi aft of carrier, lower gear when starting turn onto final.