402 - A/A - A/A missiles

Master Arm ... ON
Master Mode ... A/A

Corner speed (best sustained turn rate) ... approx 420 kts (varies with weight and altitude)

Guns -- M61A1, 578 rounds
1. Press Gray Reset Hat back to select guns.
2. If no target is locked, gun funnel is shown. Dots in the funnel are for 1000 ft and 2000 ft range. Wingspan is set on the SMS page (default is 40 ft), press the UFC OSB.
3. Radar will be automatically set to Guns Auto Acquisition Mode (GACQ). The FOV covers the HUD and will lock any target within 5 nmi range.
4. You can also use any of the other ACM modes (see below). Vertical Scan (VACQ) (Dish Hat down) is useful in a dogfight.
5. Put the pipper on the target and press Trigger to fire.

AIM-9X with HMD -- PANIC MODE -- WVR quick engagement using ACM radar and HMD
1. Press Gray Reset Hat press to select AIM-9. (Or forward for Sparrow, right for AMRAAM, backward for gun.) This automatically sets you to A/A Master Mode.
2. Press Dish Hat up to enter ACM mode with Boresight/HACQ (HMD) scan.
3. Look at target to lock with HMD.
4. Press "Uncage" (Rear Thumb Button) to allow missile to lock radar target off boresight.
5. Press Trigger to fire when you have tone.

Radar ACM Modes with Dish Hat
- U: Boresight/HACQ scan, 10 nmi range
- L-U: Boresight/LACQ scan, 40 nmi range
- D: VACQ (vertical) scan, 5 nmi range
- L: WACQ (wide) scan, 10 nmi range, 60 deg azimuth, +6/-9 deg elevation, slaved to aircraft in pitch, horizon in roll
- R: --

AMRAAM
1. Press Gray Reset Hat right to select AIM-120.
2. IN LAR vs SHOOT cue: IN LAR (Launch Acceptable Region) is on a friendly or unknown target, SHOOT is on an enemy target.
3. HUD symbology: Large circle is range scale. Going counterclockwise, diamond/square is absolute max aerodynamic range, triangle at bottom is Rmax (maximum launch range on non-maneuvering target), the next triangle is Rne (no-escape range on maneuvering target), next is Rmin (minimum launch range).
4. Press Trigger to fire.
5. After launch, HUD will show xxACT (time to active), and after it goes active ("pitbull"), shows xxTTG (time to target/impact).

Sparrow
1. Press Gray Reset Hat forward to select AIM-7.
2. IN LAR vs SHOOT cue: IN LAR (Launch Acceptable Region) is on a friendly or unknown target, SHOOT is on an enemy target.
3. HUD symbology: Large circle is range scale. Going counterclockwise, diamond/square is absolute max aerodynamic range, triangle at bottom is Rmax (maximum launch range on non-maneuvering target), the next triangle is Rne (no-escape range on maneuvering target), next is Rmin (minimum launch range).
4. If you have a target "bugged" (L&S, or primary designated target), press "Uncage" (Rear Thumb Button) to lock it with STT, or it will be STT locked automatically on launching the missile.
  - If you have no target locked and you fire a Sparrow, it will go to FLOOD mode. Missile will then guide on the closest target inside the large circle on the HUD. Uses pure pursuit guidance, so not good for crossing targets, only on targets going toward or away from you.
Press Trigger to fire.