202 - Ground - Preflight, Performance Limits

Preflight (after cold start or from hot start)
Right side:
1. Ejection Seat ... Arm (push down lever on left side of seat)
2. Lights ... CONSOLES and INST PNL knobs as desired (right console)
3. FLIR switch ... STBY or ON (T3 switch) if using TPOD so it can start warming up.
4. Radar Altimeter ... Set bug as desired (I set 100 ft)
5. HMD knob ... Full brightness or as desired (instrument panel far right)
6. IR COOL switch ... NORM (begins cooling Sidewinders, 3 hours of coolant)
7. INS knob ... IFA if year is 1986 or later, NAV if earlier (should be set by default in hot start) (right console)
Center console, bottom to top:
DISPENSER switch ... ON or BYPASS
  - ON -- Countermeasures controlled by ALE-47 system:
    1. On EW MFD page, press ALE-47 OSB to box it. It will say SF TEST, then PBIT GO, then STBY.
    2. Press MODE OSB to cycle the modes (shown under ALE-47): STBY -> MAN n -> S/A n -> AUTO
    3. Use MAN n mode (In S/A and AUTO mode the CM system automatically selects which countermeasures to use and may be wasteful).
    4. Press STEP OSB to cycle the selected program number (n). Default programs:
      - PROG #	Ch	Fl	Rpt	Int
PROG 1	1	1	10	1.0
PROG 2	1	1	10	0.5
PROG 3	2	2	5	1.0
PROG 4	2	2	10	0.5
PROG 5	1	1	2	1.0	<-- CM hat forward always triggers PROG 5
    1. To change or view program settings, press ARM OSB. Then press CHAF, FLAR, RPT, or INT OSBs and use up and down arrow OSBs to increment/decrement the number. Press SAVE OSB when finished, then RTN OSB to go back to main EW page. (OTH1 and OTH2 are for "Gen-X expendables", not yet implemented.)
    2. CM hat back triggers selected program, CM hat forward triggers PROG 5.
  - BYPASS -- Manual control. CM hat forward drops 2x chaff, CM hat back drops 2x flares.
1. ECM knob ... REC (Top Hat down)
2. RWR ... ON (ALR-67 POWER button, below center MFD)
3. EW display ... HUD (on any MFD, go to EW page, press HUD button)
4. Center MFD ... Set initial configuration (On center MFD in HSI page (default), press GAIN rocker (lower left) down about 5 times to make map overlay readable in VR. Then set to SA page and adjust range as needed.)
5. ALT switch on UFC ... As desired (shows barometric or radar altitude in the HUD)
6. IFF button on UFC... On (shows "XP" in UFC and ":4A")
7. D/L button on UFC... On
8. Radios ... As needed (click radio knobs on left or right of UFC to set channel, or tune manually)
Left side:
1. BINGO fuel amount ... As desired (IFEI Up Arrow button on engine monitor; 3000 lbs is a good start)
2. Weapons ... Begin alignment/warmup (On left MFD, go to STORES page, select weapons as needed to start alignment/warmup. JDAMs may need up to 8 minutes, Mavericks need 3 minutes.)
3. RWR volume ... As desired (Shift-E1 rotate, actual knob is by left elbow)
HOTAS:
Takeoff trim ... Press Trim Reset button (Trim Hat press), or manually +12° elevator nose up.

Performance limits
- Fuel: 10803 lbs internal
  - with 1x drop tanks (2244 lbs ea.) = 13047 lbs
  - with 2x drop tanks (2244 lbs ea.) = 15291 lbs
  - with 3x drop tanks (2244 lbs ea.) = 17536 lbs
- Flaps: 250 kts (flaps retract automatically so cannot be damaged by overspeed, but if the switch is set to FULL or HALF they will deploy under 250 kts and can make control unpredictable)
- Landing Gear: 250 kts
- Rolling speed on ground:
  - Main wheels: 210 kts
  - Nose wheel: 190 kts
- Refueling probe:
  - Extension/retraction: 300 kts
  - Extended 400 kts
- Canopy open: 60 kts
- Max speed: Mach 1.8 at 40,000 ft