302 - Flight - Advanced Navigation: Edit Waypoints and Sequences

Edit waypoint coordinates (easier than it looks, follow steps for your coordinate format)
All
1. In HSI page, press DATA OSB; starts on WYPT page with current waypoint and sequence.
2. If your new coordinate is "precise" (DDMM.MMMM, DDMMSS.SS, or MGRS 10-digit), press the PRECISE OSB (bottom row) to box it.
3. To toggle DDMM.MM vs DDMMSS (not needed if using MGRS):
  1. Press A/C OSB (top row left).
  2. Press LATLN OSB (right side bottom) to toggle DCML or SEC.
      - DCML is DDMM.MM, SEC is DDMMSS.
      - Note that this will show the coordinates for all the waypoints in the selected format. You can change the format at any time as needed.
1. Use Waypoint Inc/Dec OSBs to select waypoint to edit.
2. Press UFC OSB (left side top).
3. Follow steps in the section below for whatever coordinate format you're using, then press HSI OSB to return to main HSI page.
  - On the F10 map, use LAlt-Y to change coordinate format.
If using DDMM.MM (non-PRECISE)
1. On UFC, press POSN OSB.
2. On keypad, press 2 for N or 8 for S, then latitude in DDMM.MM format, then ENT.
3. Then press 4 for W or 6 for E, then longitude in DDMM.MM format, then ENT.
If using DDMM.MMMM (PRECISE):
1. On UFC, press POSN OSB.
2. Press 2 for N or 8 for S, then "DDMM" portion of latitude, then ENT. OSB will show ":TTHO".
3. Enter ".MMMM" portion of latitude, then ENT.
4. Press 4 for W or 6 for E, then "DDMM" portion of longitude, then ENT. OSB will show ":TTHO".
5. Enter ".MMMM" portion of longitude, then ENT.
If using DDMMSS (non-PRECISE):
1. On UFC, press POSN OSB.
2. On keypad, press 2 for N or 8 for S, then latitude in DDMMSS format, then ENT.
3. Then press 4 for W or 6 for E, then longitude in DDMMSS format, then ENT.
If using DDMMSS.SS (PRECISE):
1. On UFC, press POSN OSB.
2. Press 2 for N or 8 for S, then "DDMMSS" portion of latitude, then ENT. OSB will show ":TTHO".
3. Enter ".SS" portion of latitude, then ENT.
4. Press 4 for W or 6 for E, then "DDMMSS" portion of longitude, then ENT. OSB will show ":TTHO".
5. Enter ".SS" portion of longitude, then ENT.
If using MGRS (PRECISE or non-PRECISE)
1. On UFC, press GRID OSB.
2. Right MFD will show a grid reference display. First letter of grid increases to the right (East), second letter increases down (South).
3. Set SOI to MFD showing grid if it isn't already (Dish Hat right or wherever the grid MFD is).
4. Use TDC to slew marker to the target grid, then press TDC press. Grid square will be underlined.
  - If desired grid square is not on the display, press the OSBs by the cardinal direction labels, or press TDC press when marker is over a cardinal direction label, to move the grid.
On UFC keypad, enter the MGRS numbers (6 or 8 digits), then ENT.

Add/remove waypoints to/from a sequence
You can have up to 15 waypoints assigned to each of 3 sequences. Toggle sequences with SEQx OSB (right side bottom): cycles through SEQ1, boxed, SEQ2, boxed, SEQ3, boxed. Boxed shows lines connecting sequence waypoints on HSI map. To add/remove waypoints:
1. In HSI page, press DATA OSB; starts on WYPT page with current waypoint and sequence.
2. Change sequence if needed using SEQn OSB to sequence 1, 2, or 3.
3. Press SEQ UFC OSB (left side bottom).
4. On UFC, press INS or DEL OSB, enter number of waypoint on keypad, then ENT.
  - If inserting, new waypoint doesn't need to be in numerical order of existing points.
  - If deleting, note that the waypoint location is still saved; this just removes it from the sequence.
Press HSI OSB to return to main HSI page.