501 - A/G - Unguided Bombs, Rockets

Master Arm ... ON
Master Mode ... A/G

CCIP bombing
All
1. On left MFD, go to STORES page.
2. Select unguided bombs.
3. Set options:
  - MODE ... AUTO (CCRP level or toss) or CCIP (FD is not implemented yet, MAN is when you set the pipper depression manually)
  - MFUZ ... use NOSE or NSTL for most bombs, but see below
  - EFUZ ... As desired (INST recommended for most bombs, but see below
  - DRAG (if applicable) ... FF (Free Fall/slick) or RET (Retarded) as desired
To set ripple and interval, press UFC button. Then on the UFC itself:
  - QTY ... total number of release impulses
  - MULT ... number of bombs to be dropped per impulse
  - Total bombs dropped will be QTY x MULT.
  - INT ... interval spacing in ft
1. Put CCIP dot on the target and hold Red Button until all selected bombs are gone.
2. If there's a horizontal bar across the CCIP bomb fall line (longer than the impact crosshair line), that's the "reflected cue": actual impact point is off the bottom of the HUD. Unlike F-16 and AV-8B, holding pickle will not convert to a CCRP drop, you must either dive steeper or get to a lower altitude to make the reflected cue go away and enable bomb release.
3. For best accuracy when using CCIP, press Dish Hat up to put SOI to HUD/HMD. That will turn on AGR (Air-Ground Ranging) radar mode, and radar will be used to get exact range to CCIP impact point. When SOI is in HUD/HMD you can also press TDC press to designate a target (at VV, or HMD pipper), which will automatically switch you to CCRP mode.
Mk 20/CBU 99 Rockeye
- Buttons on SMS page:
  - MFUZ ... VT
  - Press HT OSB to cycle through burst heights (shown in columns of data in the center). 1200 or 1500 ft seems to work best.

CCRP bombing
All
1. Designate a target, either from a waypoint (WPDSG OSB on HSI or SA page), with TPOD (see other checklist), on A/G radar, or visually:
  1. Press Dish Hat up to put SOI in HUD. Shows "Ball and Chain" symbology.
  2. Put Ball and Chain pipper on target, or look at target with HMD, and press TDC press to designate. Then adjust target diamond with TDC slew if needed.
2. Once you have a target, fly toward the bomb fall line.
3. HUD shows xx REL countdown to release time, and xx.x TGT distance to target.
4. Release cue line falls from top of bomb fall line toward VV. Hold Red Button until all bombs drop.
Low level CCRP toss bombing
1. Begin pullup about 20 seconds away from target. Pull up sharply to about 15-20 deg nose up.
2. As soon as you see the release cue line start moving down the bomb fall line, stop pulling and stabilize in a steady climb, holding pickle until release.
  - IMPORTANT: If you're dropping multiple bombs in a ripple and you're still changing pitch at the moment of release, some of the bombs might not drop. This may be due to the projected interval changing too rapidly.
Pull up will start about 3.75 nmi from the target, release at about 2.5-3 nmi and 1500 ft AGL, and with a hard pull away gives closest approach about 2-2.25 nmi.

Rockets
1. On left MFD, go to STORES page.
2. Select rockets (61 is 19-shot, 68 is 7-shot, 10 is Zuni, S is Single rocket per pickle press, R is Ripple while pickle is held; Single/Ripple is set up in the mission editor, cannot be changed in flight.)
3. Press CCIP OSB to use CCIP, or MAN OSB if you want to set the pipper depression manually.
4. Press SGL OSB to launch from one pod at a time, or SAL OSB to launch from all pods of the same type.
5. For MTR OSB (at bottom), leave at M66 (MTR is rocket motor type, documentation unclear, M66 seems to be default)
6. For best accuracy when using CCIP, press Dish Hat up to put SOI to HUD/HMD. That will turn on AGR (Air-Ground Ranging) radar mode, and radar will be used to get exact range to CCIP impact point.
7. Put CCIP dot on the target and press Red Button to fire rockets.