502 - A/G - TPOD, GBU-10/12/16 Paveway II LGBs

Master Arm ... ON
Master Mode ... A/G

TPOD use
1. These steps are for the LANTIRN, but are basically the same for the ATFLIR as well.
2. Set SOI to FLIR MFD (Dish Hat toward MFD once). Special notes about tracking modes:
  - If you press Dish Hat toward the MFD when it's already SOI, it will cycle between Ground-stabilized, Area track, and Point track modes.
  - Mode is shown in upper left corner of MFD. OPR only is ground-stabilized, OPR / ATRK is Area Track, OPR / PTRK is Point Track (used for moving targets). If you are in a ATRK or PTRK, the diamond target marker shown in the HUD or HMD will be solid, otherwise it will be dashed.
  - Track is not necessary for designating target.
  - If in ATRK or PTRK mode, you cannot slew the crosshairs.
  - If you get stuck in a mode, reset by pressing Flip-down Trigger until it undesignates and slaves to Velocity Vector (VVSLAV). If you get really stuck, set FLIR switch to STBY and then back ON.
1. On FLIR page, press VVSLAV button or double-press Flip-down Trigger to slave pod to Velocity Vector.
2. Press TDC press to Ground-stabilize the pod. Can be done even if VV is above the horizon.
3. Once Ground-stabilized, use TDC slew to move crosshairs.
4. Crosshairs should have a diamond in the middle that disappears while slewing, and reappears when stopped.
5. Press Pinky Button or WIDE/NAR OSB to toggle wide/narrow view.
6. Middle-finger Hat up/down to zoom out/in (additional zoom to wide/narrow).
7. Long-press Pinky Button (or press MFD button) to toggle CCD/FLIR mode.
  - In FLIR mode, press MFD BLK or WHT button to toggle black-hot/white-hot, press ALG button to toggle automatic or manual gain control (ALG boxed is automatic gain). In manual gain, buttons on left side of MFD can be used to set gain and contrast.
1. Crosshairs move more slowly when zoomed in; to slew quickly, zoom out and/or set wide view.
2. Max visibility range is 40 nmi due to graphics rendering distance. Max laser range is 8 nmi.
Using HMD or visual designation with TPOD
  1. If you have a target designated, designation point will show as a dotted diamond in HMD.
  2. You can slew the designation either visually by setting SOI to HUD/HMD (Dish Hat up), or with the SOI on the TPOD MFD as usual.
  3. If you have no target designated yet, pressing Dish Hat up will put SOI in HUD/HMD and shows "Ball and Chain" symbology.
  4. Put Ball and Chain pipper on target, or look at target with HMD, and press TDC press to designate. Then adjust target diamond with TDC slew if needed.
  5. IMPORTANT: Press Dish Hat right to put SOI back to TPOD MFD. If you leave SOI in the HUD/HMD, slewing will be way too fast on the TPOD MFD.

GBU-10/12/16 Paveway II LGBs with TPOD (for GBU-24 Paveway III, see other page)
1. Go to STORES page (left MFD):
  1. Select bombs (82LG for GBU-12, 83LG for GBU-16, 84LG for GBU-10).
  2. MODE button ... AUTO (CCRP) (default)
  3. EFUZ button ... As desired
  4. Set laser code on bombs ... Press CODE button on MFD, press CODE button on UFC, enter code on UFC, press ENT.
  5. Press STEP button to go through the pylons and set all codes.
2. LTD/R switch ... ARM (on right hand console) (or throttle T4 switch)
3. On FLIR page (right MFD), set laser code on TPOD:
  1. Press UFC button on right of MFD (near CODE/1688) (laser must be in ARM for this to show).
  2. Press LTDC on UFC itself (must be in A/G Master Mode for this to show).
  3. Enter code on UFC keypad, press ENT.
  4. (LST and LSTC are for the Laser Spot Tracker; it can have same or different code, doesn't matter)
4. Designate target with TPOD (see steps above).
5. Fly toward bomb fall line.
6. When bomb fall line is in the HUD, HUD will show xx REL count down to drop time.
7. A few seconds before release, hold pickle until bomb drops.
8. HUD will show xx LASER countdown to laser firing; laser will fire automatically.
  - To fire laser manually instead, press TRIG button on FLIR MFD, then fire laser with joystick trigger. Bomb will immediately turn directly toward laser and trajectory will be affected, so use with care. Lasing normally starts about 10 seconds before impact.
1. When laser is firing, HUD will show xx TTI countdown to Time To Impact.
2. You can adjust the crosshairs on TPOD as needed before bomb impacts.
3. Before setting up next bomb run, re-arm laser if needed.

Valid laser codes:
Format is ABCC, A=1, B=1-7 (or 1-6 in DCS??), C=1-8, never 0 or 9. Range should be 1111 to 1788 but may be 1111 to 1688 in the game. Some planes in DCS (A-10C?) may not be able to set B=7.