510 - A/G - AGM-141 TALD

Master Arm ... ON
Master Mode ... A/G

AGM-141 TALD -- WIP, steps unverified
1. On left MFD, go to STORES page, select 82P.
2. Press Red Button to launch. They will automatically spread out slightly to avoid collisions.

TALD flight profile:
1. After launch, will maintain heading and altitude until TAS is 360 kts (6 nmi per min).
2. Begin descent, maintaining 360 kts TAS, until 3,200 ft MSL.
3. Maintain 3,200 ft until stall, and fall to ground.

Flight time at 360 kts TAS (not accounting for initial higher speed, or final slow descent):
10 nmi	1m40s
20 nmi	3m20s
30 nmi	5m0s
40 nmi	6m40s
50 nmi	8m20s
60 nmi	10m0s

Tested ranges from RedKite video (ISA conditions, no wind):
Release	TALD altitude (ft) at range, and final range
	10 nmi	20 nmi	30 nmi	40 nmi	50 nmi	60 nmi	70 nmi	80 nmi	90 nmi
45k ft, 260 IAS / M 0.93	44,813	39,851	33,760	27,614	20,993	13,654	4,847	2,109	82 nmi
40k ft, 330 IAS / M 1.05	39,820	36,064	29,982	23,551	16,506	8,390	3,273	76 nmi
30k ft, 500 IAS / M 1.25	29,770	25,477	18,664	10,964	3,274	58 nmi
20k ft, 538 IAS / M 1.11	19,704	12,659	3,966	921	41 nmi
10k ft, 567 IAS / M 1.00	8,000	3,273	25.5 nmi
5k ft, 600 IAS / M 1.00	3,272	19 nmi