997 - NS430 GPS navigation system

Shift-E2 press to open 2D display. Integrated in cockpit for C-101, L-39 (Mission Editor must be set to dismount gunsight), Mi-8, and Gazelle.

Basic use
- Turn on with C knob at top left. Press ENT, then press ENT again to go past the self-test screen.
- Use left knobs and buttons to set voice and VOR frequencies. Press PUSH C/V to change which frequency fields will be edited when turning the left knob.
- Press PUSH CRSR to toggle a cursor. With cursor active, use Large Right Knob to move cursor or change fields, Small Right Knob to change field values.
- At any time, press and hold CLR for 2 seconds to return to main NAVdef page.
- CDI button toggles navigation info source between GPS and VOR (VLOC).
- OBS button toggles whether waypoints are automatically incremented when flying over them.
- MSG button shows messages, press CLR to clear them (when they're showing).
- FPL button shows flight plan page. (First create waypoints, then add them to the flight plan.)
- PROC button shows procedures.
- Use Large Right Knob to change blocks, Small Right Knob to change pages within block.
- Blocks (page groups) and pages:
NAV	WPT	AUX	NRST / (Caucausus region only)
NAVdef - Default nav page, shows from/to waypoints, course deviation (CDI), ground speed, etc.	WPTapt aka WPTero - Airport information.	AUXfpl - Flight plan page.	NRSTaero - Nearest airports.
NAVmap - Basic map.	WPTrunway - Runway info for the selected airport.	AUXutil - Various utilites: timer, checklists, trip statistics, sunrise/sunset.	NRSTint - Nearest intersections.
NAVterrain - Map with terrain colored by altitude.	WPTfreq - Radio and ILS frequency info ditto.	AUXsetup1 - Setup options 1: CDI scale, units, lat/long format, date/time format.	NRSTndb - Nearest NDBs (Non-Directional Beacon).
NAVcom - Nearest airport arrival/departure frequencies.	WPTapr - Approach procedures ditto.	AUXsetup2 - Setup options 2: display brightness/contrast, nearest airport settings.	NRSTvor - Nearest VORs.
NAVpos - Your current position.	WPTarr - Arrival procedures ditto.		NRSTuser - Nearest user-defined waypoints.
NAVsat - GPS satellites and position error.	WPTdep - Departure procedures ditto.		NRSTartcc - Nearest air traffic control centers.
NAVvprof - Set up waypoint height and vertical speed required.	WPTint - Intersection info.		NRSTfss - Nearest flight service stations.
	WPTndb - NDB (Non-Directional Beacon) info.		NRSTspace - Nearest controlled airspaces.
	WPTvor - VOR info.
	WPTuser - Info for user-defined waypoints.

Set a Direct-To waypoint on the map
1. If not already on the map page: Press and hold CLR for 2 seconds to return to NAVdef page, turn Large Right Knob to go to NAVmap page.
2. Press PRESS CRSR to show arrow cursor on the map.
3. Turn Large Right Knob and Small Right Knob to move the arrow cursor over the desired destination (can be anywhere on the map, doesn't have to be a map icon).
4. Press the DIRECT-TO (D-arrow) button to show the DIRECT-TO WAYPOINT page.
5. Press ENT to confirm and ENT again to begin navigation to waypoint.

Set the map to show Track-up instead of North-up
1. If not already on the map page: Press and hold CLR for 2 seconds to return to NAVdef page, turn Large Right Knob to go to NAVmap page.
2. Press MENU.
3. Press ENT to select "Setup Map?".
4. "North up" should be flashing. Press ENT to change it to "Track up".

Find an airport by ICAO code or name
TODO