998 - Sustained turn rates

Rates are rounded down (floor) to integer degree. Tested at 1000 m (3281 ft) with 50% fuel, no weapons (but with pylons), flaps up or in auto as noted. Speeds are IAS. Data from https://dcs.silver.ru .

In max rate order descending:
F-14B, F-15C, F-18/JF-17/MiG-15, MiG-29/Su-27, F-14A/F-16C/M2000, F-86/Su-33, AV-8B, AJS37/F-5E/MiG-21

- AJS37 -- 13 deg/s from 550-770 kph|0.48-0.67 M (peak at 660 kph|0.57 M). Rate is pretty flat throughout speed range, 12 deg/s at 470 kph|0.40 M, increasing up to max rate, and falling back through 12 deg/s at 1050 kph|0.91 M.
- AV-8B -- Flaps Auto/Nozzles 0: 15 deg/s at 245-285 kts|0.39-0.46 M (peak at 255 kts|0.41 M). Flaps Auto/Nozzles 10: 15 deg/s at 220-300 kts|0.36-0.48 M (peak at 245 kts|0.40 M), rate is slightly better with Nozzles 10 up to 325 kts|0.52 M, same after that. Flaps Cruise (forced up) decreases turn rate significantly under 330 kts|0.53 M, and increases it significantly over 330 kts|0.53 M (peak at 335 kts|0.54 M, 14.5 deg/s) up to 500 kts|0.8 M. Ideally, use Flaps Auto/Nozzles 10 up to 330 kts, then Flaps Cruise if forced to fight faster than that.
- F-14A -- 17 deg/s from 475-530 kts|0.76-0.85 M (peak at 500 kts|0.81 M). Rate is over 16.5 deg/s from 375-475 kts|0.60-0.75M.
- F-14B -- 21 deg/s from 545-565 kts|0.87-0.90 M (peak at 560 kts|0.90 M). 17 deg/sec from 305-460 kts|0.49-0.74 M (with a slight dip from 340-360 kts|0.55-0.58 M due to auto flaps), then increases from there to the peak.
- F-15C -- 20 deg/s from 525-550 kts|0.85-0.89 M (peak at 543 kts|0.87 M). 15 deg/s at 180 kts|0.29 M, 16 deg/s at 220 kts|0.35 M, 17 deg/s at 285 kts|0.46 M, 18 deg/s at 405 kts, 19 deg/s at 505 kts, then a sharp peak up to max rate. Falls off quickly, back to 15 deg/s at 635 kts|1.02 M.
- F-16C -- 17 deg/s from 455-535 kts|0.73-0.85 M (peak at 535 kts|0.85 M) (max tested speed). Rate increases steadily with speed, 15 deg/s at 285 kts|0.46 M, 16 deg/s at 335 kts|0.54 M, and continuing up from there.
- F-18C -- 19 deg/s from 435-455 kts|0.70-0.73 M (peak at 445 kts|0.72 M). Rate increases steadily with speed, 16 deg/s at 240 kts|0.39 M, 17 deg/s at 280 kts|0.45 M, 18 deg/s at 345 kts|0.55 M.
- F-5E -- 13 deg/s from 265-530 kts|0.43-0.85 M (peak at 473 kts|0.77 M, 13.9 deg/s). Mostly flat, increasing with speed until peak at 335 kts|0.53 M (13.6 deg/s), then flaps move and rate drops slightly, increasing steadily again until max. Turn rate is higher than the MiG-21 from 245-545 kts|0.39-0.87 M, lower outside that range.
- F-86 -- 16 deg/s from 235-400 kts|0.37-0.64 M (peak at 325 kts|0.52 M). Turn rate is lower than the MiG-15 from 220-435 kts|0.35-0.70 M, higher outside that range, especially at higher speeds.
- JF-17 -- 19 deg/s from 300-325 kts|0.48-0.52 M (peak at 315 kts|0.50 M) and again from 385-430 kts|0.62-0.68 M (peak at 430 kts|0.68 M) (max tested speed), dipping slightly in between to 18.8 deg/s at 345 kts|0.56 M. Note that G-limiter kicks in at Mach 0.8. 15 deg/s at 185 kts|0.28 M, 16 deg/s at 200 kts|0.32 M, 17 deg/s at 240 kts|0.39 M, 18 deg/s at 280 kts|0.45 M.
- MiG-15 -- 19 deg/s from 510-640 kph|0.45-0.56 M (peak at 560 kph|0.49 M). Turn rate is higher than the F-86 from 400-800 kph|0.35-0.70 M, lower outside that range, especially at higher speeds.
- MiG-21 -- 13 deg/s at 400 kph|0.34 M or lower, then stays pretty flat in the 12s (low at 600 kph|0.50 M, 12.4 deg/s) until 1050 kph|0.91 M where it drops rapidly. Turn rate is lower than the F-5 from 450-1010 kph|0.39-0.87 M, higher outside that range.
- MiG-29 -- 18 deg/s from 640-850 kph|0.55-0.73 M (peak at 850 kph|0.73 M) (max tested speed). Rate increases steadily with speed, >15 deg/s at 370 kph|0.32 M, 16 deg/s at 420 kph|0.37 M, 17 deg/s at 510 kph|0.44 M.
- Mirage 2000 -- 17 deg/s from 380-455 kts|0.61-0.72 M (peak at 455 kts|0.72 M) (max tested speed). Rate is mostly flat from 170 kts|0.27 M, slightly increasing with speed. 16 deg/s at 170 kts|0.27 M (peak at 240 kts|0.38 M).
- Su-27 -- 18 deg/s from 880-950 kph|0.76-0.82 M (peak at 920 kph|0.80 M). 15 deg/s at 370 kph|0.32 M, 16 deg/s at 470 kph|0.41 M, 17 deg/s at 670 kph|0.58 M, dipping slightly to 16.8 deg/s at 840 kph|0.72 M before rising again up to peak rate.
- Su-33 -- 16 deg/s from 880-1020 kph|0.76-0.88 M (peak at 902 kph|0.80 M). 14 deg/s at 430 kph|0.37 M, 15 deg/s at 580 kph|0.50 M, peak at 700 kph|0.60 M (15.3 deg/s) and dipping slightly to 14.9 deg/s at 860 kph|0.74 M before rising again up to max rate.