1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

301 - Flight - Navigation, Autopilot, Flight performance

Navigate to a lat/long -- WIP
1. Create waypoint:
  1. Press NAV CTRL on knee computer
  2. Press INC/DEC buttons to select waypoint.
  3. Enter northing on keypad, format is "NDDMMSSS" or "SDDMMSSS" (note no decimal point), then press OSB next to northing line.
  4. Enter easting on keypad, format is "EDDDMMSSS" or "WDDDMMSSS" (note no decimal point), then press OSB next to easting line.
2. Distance and bearing will be shown on the knee computer screen, and should also be shown on HSI MFD page. If not shown there, increment and decrement waypoint to re-select it.
3. Press NAV AP button to have AP fly to the waypoint.
4. May need to manually enter a wind value? Or plane will drift off heading?

Autopilot -- WIP
Climb to altitude and hold:
  1. Set desired altitude with ALT SEL knob. Selected altitude appears above current altitude on HUD and MFD.
  2. Start climbing, then engage the VS HOLD AP.
  3. Then engage the ALT SEL AP.
  4. This will hold the current climb rate until the selected altitude is reached.
You can also set an airspeed to hold using the IAS knob, which will hold the airspeed by climbing more or less steeply, see best climb speed table below.

Flight performance data
Best climb speed
Gross weight (x1000 lbs)	Speed (kts IAS)
100	143
110	148
120	154
130	159
140	165
150	171
160	176
170	182
180	187

Best true airspeed: 22,500 ft (see performance manual page 182, Flight Limit Speeds)