1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

102 - Controls - Throttle Grip
U=Up, D=Down, F=Forward, B=Backward, L=Left, R=Right, P=Press, S-*=Shift-*, L-*=Long-*

Top Hat -- "T2"
- F/B: Dispense countermeasures
- U: Toggles jammer on/stby
Top Hat Ring
Rotate: --
Middle Hat -- "T4"
- U: (SRS radio 1 PTT)
- D: (SRS radio 2 PTT)
- F: (SRS radio 3 PTT)
- B: IFF Interrogator start/stop
Bottom Hat -- "T3"
- F: Extend speedbrakes (single press fully extends)
- B: Retract speedbrakes (single press fully retracts)
Front Thumb Button
- P: Engine mode switch to CMBT (a little more power in exchange for a little more engine wear)
- S-P: Engine mode switch to C+T (normal setting)
Rear Thumb Button
P: AG Manual Mode, DGFT Missile Designator Control
Bottom Thumb Button
- P: Thottle Stop->Idle
- S-P: Throttle Idle->Stop
Ministick -- "T5/TDC"
Axes: Slew TCD on SOI
P: Lock target
Middle Finger Hat -- "Sensor (WMD/TV)"
- U/D: Radar antenna elevation up/down, TPOD zoom in/out
- L/R: Adjust TPOD gain (brightness), maybe other functions??
- P: --
Ring Finger Slider
U/D: --
Pinky Switch -- "T1" Master modes
- U: INTC (Intercept or A/A) Master Mode
- D: A/G Master Mode
- P: NAV Master Mode
Pinky Button
P: Laser Designator On/Off??
Pinky Wheel
- Rotate F: --
- Rotate B: --
- P: Exterior Light Master Switch - Normal/Off (toggles external lights)